| Safe Work Method Statement (SWMS) Part 1 |
| --- |
| Activity: Manual Handling (building) | SWMS #: |
| Business Name: Bowley Plumbing Services | ABN: 97 007 937 439 |
| Business Address: 19 Swallow Ave, Modbury Heights SA |
| Business Contact: Phillip Bowley | Phone #: 0418 891 498 |
| SWMS Approved by: Employer / PCBU / Director / OWNER. |
| Name: Phillip Bowley |
| Signature: | Date: |
| Person/s responsible for ensuring compliance with SWMS: Phillip Bowley and all employees |
| Person/s responsible For reviewing the SWMS: Phillip Bowley |
| Relevant workers consulted in the development, approval and communication of this SWMS. | All Persons involved in the task must have this SWMS communicated to them before work commences. |
| Name | Signature | Date | Tool Box Talks will be undertaken to identify, control and communicate additional site hazards. |
| B Small |  |  | Work must cease immediately if incident or near miss occurs. SWMS must be amended in consultation with relevant persons. |
| M Fitch |  |  | Amendments must be approved by Phillip Bowley and communicated to all affected workers before work resumes. |
| T Dawson |  |  | SWMS must be made available for inspection or review as required by WHS legislation. |
|  |  |  | Record of SWMS must be kept as required by WHS legislation (until job is complete or for 2 years if involved in a notifiable incident). |
| Principal Contractor Details (The builder or the organisation you are working for.) |
| Principal Contractor (PC): | Project Name: | Date SWMS provided to PC: |
| Project Address: |
| Project Manager (PM): | PM Signature: | CONTACT PH. #: |
| SWMS Scope: This SWMS covers general aspects associated with hazardous manual handling tasks in the building industry. |

| This work activity involves the following “High Risk Construction Work” |
| --- |
| ☐ Confined Spaces |  Mobile Plant | ☐ Demolition | ☐ Asbestos |
| ☐ Using explosives | ☐ Diving work | ☐ Artificial extremes of temperature | ☐ Tilt up or pre-cast concrete |
| ☐ Pressurised gas distribution mains or piping chemical, fuel or refrigerant lines energised electrical installations or services |
| ☐ Structures or buildings involving structural alterations or repairs that require temporary support to prevent collapse |
| ☐ Involves a risk of a person falling more than 2m, including work on telecommunications towers |
| ☐ Working at depths greater than 1.5 Metres, including tunnels or mines | ☐ Work in an area that may have a contaminated or flammable atmosphere |
| ☐ Work carried out adjacent to a road, railway or shipping lane, traffic corridor | ☐ In or near water or other liquid that involves risk of drowning |
| Likelihood | Insignificant | Minor | Moderate | Major | Catastrophic | Score | Action | HIERARCHY OF CONTROLS | Most Effective |
| Almost certain | 3 High | 3 High | 4 Acute | 4 Acute | 4 Acute |  |  |  |  |
| Likely | 2 Moderate | 3 High | 3 High | 4 Acute | 4 Acute | 4A Acute | DO NOT PROCEED. |  |  |
| Possible | 1 Low | 2 Moderate | 3 High | 4 Acute | 4 Acute | 3H High | Review before commencing work. |  |  |
| Unlikely | 1 Low | 1 Low | 2 Moderate | 3 High | 4 Acute | 2M Moderate | Maintain control measures. |  |  |
| Rare | 1 Low | 1 Low | 2 Moderate | 3 High | 3 High | 1L Low | Record and monitor. |  | Least Effective |
| Personal Protective Equipment (PPE): Ensure all PPE meets relevant Australian Standards. Inspect, and replace PPE as needed. |
| Foot Protection | Hearing Protection | High Visibility | Head Protection | Eye Protection | Face Protection | Hand Protection | Protective Clothing | Breathing Protection | Sun Protection | fall Arrest | Rings, watches, jewellery that may become entangled in machines must not be worn. Long and loose hair must be tied back. |
|  | ☐ |  | ☐ | ☐ | ☐ |  | ☐ | ☐ | ☐ | ☐ |  |
| AS 1319-1994 Safety signs for the occupational environment reproduced with permission from SAI Global under licence 1210-c062. Standards may be purchased at http://www.saiglobal.com |

| Job Step | Potential Hazard/s | IR | Control Measures to Reduce Risk | RR | Responsible Person |
| --- | --- | --- | --- | --- | --- |
| Inherent Risk-rating (IR) Residual Risk-rating (RR) |
| Conduct a risk assessment identifying potential hazardous manual tasks | Musculoskeletal (MSD) injuries  Muscles, ligaments, nerves, tendons in the wrists, arms, shoulders, neck or legs, muscles, ligaments or discs in the back. Muscular Stress  sprains, strains, temporary soft tissue injuries Indirect Injuries  cuts / lacerations. | 3H |  | Using the Hazardous Manual Task Risk Assessment Form supplied in this SWMS identify your work activity and potential risks Follow the associated controls within this SWMS for the activity If you identify any hazard that is not covered in this SWMS, stop the activity Ensure a safe work method is developed for the task, in consultation with relevant parties, before recommencing the activity Ensure realistic work rates and adequate numbers of workers for the task Add the additional control to this SWMS. | 2M |  |
| Training and Capabilities | Lack of training or the assessment of capability may lead to personal injury, property damage &/or environmental incident. | 3H | Ensure all persons entering site have a General Construction Induction Card (white card). Ensure all relevant workers have undertaken training and/or received instruction in the use of control measures. Include: Manual handling All workers are trained in this SWMS Reporting procedures for incidents Correct use of equipment including selecting, fitting, use, care of and maintenance Correct use of all tools used Use of supervision where required (e.g. new starters or new equipment) Ensure supervisors, foremen etc. are suitably experienced in the type work to be conducted. | 2M |  |
| Work area set up, placement of equipment and materials & construction installations e.g. plasterboard, painting, concrete etc. | Pushing, pulling, lifting, carrying, setting down, | 3H | Use mechanical aids wherever possible. Ensure: Working vehicle is suitable for the task of transporting tools, materials etc. e.g. van, utility - avoid lifting equipment from the boot of a sedan Trolleys / ramps are used where required to remove equipment from vehicles and transfer of materials and equipment to the work area Licensing required for relevant powered mobile plant such as forklifts All operators to be trained and competent in the use of mechanical aids Use in accordance with manufacturers instructions Training to include: Check that the lifting aid is correct type and size for the intended work Pre-inspection requirements Safe Load Limit (SLL) or Safe Working Load (SWL) Positioning of items on the aid Safe movement of the aid Potential hazards in the work zone (plant /vehicles/people) Set up work area to minimize travel distance with loaded aid. When using a lifting aid, ensure: Push rather than pull the aid Do not pull large loads towards yourself Do not jerk to get the aid moving Seek assistance if the load is too heavy or break down the load to make it lighter Never try to move or push a loaded aid or skid by hand Use proper lifting techniques when loading and unloading When going down an incline push, don't pull. Ensure regular maintenance and service of equipment and tools can reduce the force required to operate them. Where persons are required to lift without lifting aids, ensure: Lift within physical capabilities of individual Weight of object is known, avoid lifting loads more than 16 – 20kg. Extreme force will not be required Object can be held close to body (this excludes large/bulky items that are difficult to grasp, or hot/cold objects that cannot be held against body) Flat, even floor surface, short travel distance with no obstructions. Sufficient lighting Suitable weather conditions (example: large cement sheeting can be unsafe to lift in high winds) Objects to be lifted are in suitable condition (dry, stable, even distribution of weight, handles where possible, allows good grip, will not block vision, no sharp edges, containers sealed, no chemical or other waste residue on object, etc.) Objects will not be lifted up/down ladders Repetitive lifting will not exceed 30 minutes at a time or 2 hours over entire shift Suitable personal protective equipment (PPE) provided (example: snug-fitting furniture removalist gloves, safety shoes with non-slip soles). Where Team Handling required (as last resort). Ensure: All members of team-lift are matched in size, skills, capabilities Number of persons proportionate to weight of load and level of difficulty Lifts are planned and rehearsed Person allocated to plan and be in charge of lift – all others to know their roles Sufficient space to maneuver Use aids where possible (lifting bars, handles etc.) | 2M |  |
|  | Poor lighting awkward postures and movements | 3H | Adequate lighting for internal works Lighting for night works Keep lights and light fittings clean Bring the work closer to the operator. |  | 2M |  |
|  | Incorrect height and placement of equipment etc.  poor posture, movements and forces |  | Use adjustable work stations to accommodate the different heights of workers Work station is set-up ergonomically where possible (avoid reaching too high, low, over-reaching or other awkward postures) Provide trestles / benches to place work pieces on to reduce manual handling risks (between shoulder and knee height) |  |  |
|  | Unnecessary manual handling | 3H | Housekeeping - keep work area clean, tidy and clutter free. Ensure materials / equipment is as close to work area as possible. | 2M |  |
|  | Exposure to cold conditions  |  | Adequate onsite amenities providing water, warm drinks and shelter for breaks Job rotation. |  |  |
|  | Heat Exposure  |  | Locate work area as far away as possible from sources of heat and hot processes Provide screening Adequate ventilation If working indoors add fans for air circulation Alter work schedule so that the work can be done in the cooler part of the day Provide cool, well ventilated area for breaks Provide drinking water. |  |  |
| Operating non-mobile plant e.g. jackhammers, power tools, powder actuated tools etc. | Vibration  Raynauds Syndrome/White Finger | 3H | Provide tools with anti-vibration or anti-kickback features where possible Use shock-absorbing gloves as required (particularly in cold weather) Use smallest tool needed for the task Ensure all handles have appropriate grip covers installed e.g. rubber handlebar grips, not bare metal Ensure standing on firm surface (standing on loose/unstable objects can accentuate vibration. | 2M |  |
|  | Repetitive and sustained tasks  | 3H | Ensure: | Job rotation Sufficient breaks | Suspend / support heavier tools if used repetitively Mount tools e.g. drill stand. | 2M |  |
|  | Indirect Injuries  cuts / lacerations, blisters | 3H | Ensure handles: | Comfortable grip No sharp edges. | 2M |  |
|  | Pushing, pulling, throwing, pressing objects, high grip forces additional forces on the hand, arm or wrist |  | Tools and equipment used: Select suitable size, weight, type of handle, grip etc. Ensure triggers are long enough (approx. 5cm long) to allow activation by several fingers Use triggers that can lock into place for use over longer periods (more than 30 seconds at a time) Ensure handles: Are cylindrical and approx. 4cm in diameter Allow wrist to remain straight Comfortable grip Grip length approx. 12cm. |  |  |
|  | Exposure to cold conditions  |  | Working outdoors. Ensure: Appropriate protective clothing Encourage workers to have adequate warm drinks Wear hand protection Wear non-slip footwear (slippery surfaces) | Access to warm shelter during breaks Adequate breaks Check weather conditions – do not work in extreme cold. |  |  |
|  | Heat Exposure  |  | Working outdoors. Ensure: Suitable protective clothing Sun brim on hard hat Safety glasses - UV Rated Use 30+ sunscreen on exposed skin areas | Adequate drinking water Access to shade during breaks Adequate breaks Check weather conditions – do not work in extreme heat. |  |  |
|  | Fatigue and shift work  |  | Adequate breaks during a shift for muscle recovery Adequate time between shifts for rest and recuperation Job rotation Where employees work shifts are longer than 8 hours, the pace and duration of repetitive work or sustained effort should be reviewed and reduced where necessary. |  |  |
|  | Over reaching | 3H | Use tools with extendable handles e.g. pole sander for sanding plasterboard. | 2M |  |
| Operating powered mobile plant | Poor driver posture  muscles, ligaments, nerves, and tendons in the wrists, arms, shoulders, neck or legs, muscles, ligaments or discs in the back. | 3H | Ensure: Seat edges are rounded so the edges do not press into the thighs Seat covering should allow air to circulate. Never jump from cabin. Access/exit using steps and hand rails. A vehicle's interior must be adjustable so drivers of different heights and shapes can: Reach the pedals and controls Have sufficient headroom Sit high enough to see out the front and side windows and mirrors Reach the steering wheel without stretching the arms. Adjust controls and seating: Steering Wheel: Objects and controls to be in easy reach to prevent unnecessary reaching Elbows and shoulders relaxed with hands positioned below shoulder level Headrest: Position centrally behind the head Mirrors: The rear view and side mirrors to ensure adequate vision of surrounding areas. Seat Height: Raise to ensure maximum road vision Ensure adequate clearance from roof Lower Limb Position: Knees bent comfortably to operate foot pedals Steering wheel should not touch top of legs Seat Plan: Thighs supported along length of cushion Avoid pressure behind knees Back Rest: Shoulders slightly behind hips Lumbar Support: A S-shape spine is a safe shape. DO NOT store items in back pockets of your pants e.g. do not keep your wallet in back pocket. | 2M |  |
|  | Whole body vibration   | 3H | Refer to manufacturers manual regarding vibration with the selected tool Adjust existing vibration damping mechanisms Install a vibration isolating device where practicable / possible Avoid uneven or loosely compacted roads as much as possible in travel plan. Ensure regular maintenance and service of equipment and tools can reduce the force required to operate them. | 2M |  |
|  | Exposure to heat and cold conditions  |  | Adequate onsite amenities providing water, warm drinks and shelter for breaks Ensure vehicle cabin is air conditioned Appropriate protective clothing Check weather conditions – do not work in extreme weather. |  |  |
|  | Driving in wet conditions  |  | Check weather conditions – do not work in extreme weather Conduct vehicle pre-inspection as per manufacturers instructions Ensure good tyre tread Vehicle lights are working Windscreen and lights are clean Drive slowly avoiding aquaplaning and skidding Drive with your lights on low beam (it is easier to see with low beam in fog) Use your air conditioner or demister to keep your windscreen clear of condensation Double the distance between you and the car in front Avoid breaking suddenly or accelerating or turning quickly reducing your chances of skidding Avoid driving on unsealed roads Use road line markings to stay in the middle of your lane—in wet weather it is more important than ever to stay in the correct position on the road Do not drive on roads covered with water (even partially covered) Watch out for soil movement. |  |  |
|  | Fixed seat in a forward position  repetitive or sustained twisting of the neck and body when reversing |  | This risk is prevalent in road making machinery. Ensure vehicle has: Swivel seat mount Two sets of controls or, controls that move with the seat. |  |  |
|  | Visibility problems  |  | Ensure mirrors are undamaged and clean Install visual aids such as revering cameras. |  |  |
|  | Fatigue and shift work  |  | Adequate breaks during a shift Adequate time between shifts for rest and recuperation. |  |  |
|  | Prolonged seating   | 3H | Ensure the driver: Adequate breaks throughout the shift to allow for movement e.g. go for a walk Does not exceed regulated driving hours Provide adequate lumber support. | 2M |  |
| Working near powered mobile plant | Contact with mobile plant or passing vehicle | 3H | Check constantly for changing hazards while working and monitor work position at all times. Ensure: High visibility clothing worn at all times Do not stand behind reversing vehicles Allow sufficient distance from plant during operation (allow sufficient room for equipment failure – such as arm/boom failure or plant rollover) No work is conducted in established “no go zones” for pedestrians Alertness at all times. Listen for: Reversing alarms/beepers Calls from Plant Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Work positions should be in clear sight of plant operators Follow traffic management plan requirements. NOTE: Some traffic management plans may say that pedestrians have right-of-way. Never assume this. Make visual and verbal contact with plant operator as required. | 2M |  |

| Emergency Response - Call 000 immediately. |
| --- |
| If work is to be conducted on a construction site (or a site controlled by another Employer / PCBU) follow the site-specific Emergency Management Plan. Ensure: Adequate numbers of first aid trained staff are on site when working at heights occurs First aiders are trained and competent in managing injuries associated with demolition until emergency services arrive All rescue equipment is in good condition, available for use and in close proximity to the work site. | Ensure workers have access to: First aid kit/supplies First Aid trained personnel familiar with Resuscitation and emergency response for electric shock M/SDS Communication devices (check mobile phones will have service in area) Suitable fire protection equipment. |
| Safe Work Method Statement (SWMS) Part 2 |
| Formal Training, Licences required for workers undertaking this task: | Relevant Legislation & Codes of Practice Retain only the legislation references applicable to your state of operation for this SWMS. |
| Delete or add as relevant Licence to Perform High Risk Work (operating certain plant, equipment) TAFE or other recognised training organisation Construction Induction Card (or equivalent) Competent in operation of make/model of plant Emergency procedures – emergency response PPE Traffic Management Plans | Commonwealth, NSW, QLD, ACT Work Health and Safety Act 2011 Work Health and Safety Regulations 2011 Northern Territory Work Health and Safety (National Uniform Legislation) Act 2011 Work Health and Safety (National Uniform Legislation) Regulations SA, Tasmania Work Health and Safety Act 2012 Work Health and Safety Regulations 2012 Codes of Practice: Safe Work Australia (2011): Construction Work Managing the Risk of Plant in the Workplace How to Manage Work Health and Safety Risks Hazardous Manual Tasks WHS Consultation, Cooperation & Coordination Managing the Work Environment and Facilities | Victoria: Occupational Health & Safety Act 2004 Occupational Health & Safety Regulations 2007 Compliance Codes: WorkSafe Victoria (2008): Compliance Code: Communicating OHS Across Languages Workplace Amenities and Work Environment Codes of Practice: WorkSafe Victoria (1990): No. 13: Building and Construction Workplaces (2000): No. 25: Manual Handling (1995): No. 19: Plant (1998): No. 23: Plant (Amendment No. 1) Western Australia Occupational Safety & Health Act 1984 Occupational Safety & Health Regulations 1996 Codes of Practice: |
| Details of Supervisory Arrangements for workers undertaking this task: |  |  |
| Delete or add as relevant Suitably qualified supervisors for job Direct on-site supervision Remote site – communication systems/ schedule Audits Spot Checks, etc. Reporting systems |  |  |
| Details of: regulatory permits/licenses Engineering Details/Certificates/WorkCover. Approvals: |  |  |
| Delete or add as relevant Local council permits Authorisation to work Confined Space Permit Building Approvals EPA approvals/permits Certain plant to be registered with State Authority PPE to comply with relevant Australian Standards |  |  |
|  | Plant/Tools/Equipment List for the job. | Reference Documents |
|  | (Make & Model) |  |

| Safe Work Method Statement (SWMS) Part 3 |
| --- |
| This SWMS has been developed in consultation and cooperation with employee/workers and relevant Employer/Persons Conducting Business or Undertaking (PCBU). I have read the above SWMS and I understand its contents. I confirm that I have the skills and training, including relevant certification to conduct the task as described. I agree to comply with safety requirements within this SWMS including risk control measures, safe work instructions and Personal Protective Equipment described. |
| Overall Risk Rating after Controls | 1 Low | 2 Moderate | 3 High | 4 Acute |
| Employee/Worker Name | Job Role / Position | Signature | Date | Time | Employer/PCBU/ Supervisor |

| Review: Ensure all controls are reviewed as per the following: If controls fail to reduce risk adequately When changes to the workplace or work activity occur that create new / different risks where controls may no longer be effective New hazards identified After an incident involving work activities relevant to this SWMS During consultation with relevant persons indicate review is needed A Health and Safety Representative (HSR) requests a review in line with the requirements of the legislation. | Monitor: To ensure controls are implemented and monitored effectively: Toolbox /pre-work meetings will be undertaken Relevant persons will be consulted on hazards and contents of SWMS, work plans and other applicable information Control measures will be monitored throughout works: *Spot checks *Consultation *Scheduled audits Corrective actions will be recorded and rectified in a timely manner SWMS will be reviewed and updated accordingly (in consultation with relevant persons). |
| --- | --- |
| Review No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Name: |  |  |  |  |  |  |  |  |  |  |
| Initial: |  |  |  |  |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |  |  |  |  |

hazardous manual task risk assessment form

| Location of Task: | Management Rep: | Date of assessment: |
| --- | --- | --- |
| Description of hazardous manual task: | Health and Safety Rep: |
|  | Workers, others (consultants etc.): |
| Reason for Identification: | Existing task New task Change in task, object or tool Report of musculoskeletal disorder (MSD) New information | Does the task involve: | Postures Forces Repetitive movements Sustained movements | As a guide; Repetitive means the movement or force is performed more than twice a minute Sustained means the posture or force is held for more than 30 seconds at a time. |

| Environmental Factors | Yes | No | N/A | Where ‘yes’ is ticked enter control option/s from Column 6 or enter alternative control/s | Column 6 - Control options. (These are example risk controls and the list is not exhaustive). |
| --- | --- | --- | --- | --- | --- |
| Example: Is their hand, arm or whole body vibration? |  | ☐ | ☐ | M & O | Automate or isolate processes Use remote controlled processes to isolate workers from vibration sources Isolate workers from vibration sources through the use of dampening or suspension systems Redirect cold exhaust air Improve ventilation and air circulation Provide shade Provide thermal screens/barriers Provide sheltered walkways/wind barriers Provide lighting suited to the task Insulate hot/cold items or tools Select alternative lower vibration equipment Use balancers/tensioners Use vibration damping materials Maintain equipment Provide rest breaks and task variation Ensure workloads and deadlines are achievable Allow workers some latitude to influence the rate and pace of work Monitor and control overtime and shiftwork Provide training and supervision |
| Is their hand, arm or whole body vibration? | ☐ | ☐ | ☐ |  |  |
| Hot working conditions | ☐ | ☐ | ☐ |  |  |
| Cold working conditions | ☐ | ☐ | ☐ |  |  |
| Wet working conditions | ☐ | ☐ | ☐ |  |  |
| Workers being jolted or continuously shaken | ☐ | ☐ | ☐ |  |  |
| Driving for long periods | ☐ | ☐ | ☐ |  |  |
| Driving on rough roads | ☐ | ☐ | ☐ |  |  |
| Frequent use of hand powered tools or use for long periods | ☐ | ☐ | ☐ |  |  |
| Using high grip forces or awkward postures when using power tools | ☐ | ☐ | ☐ |  |  |
| Use of machines or tools where the manufacturer’s handbook warns of vibrating | ☐ | ☐ | ☐ |  |  |

| Postures and Movements | Yes | No | N/A | Where ‘yes’ is ticked enter control option/s from Column 6 or enter alternative control/s | Column 6 - Control options. (These are example risk controls and the list is not exhaustive). |
| --- | --- | --- | --- | --- | --- |
| Bending or twisting the back forwards, sideways or backwards | ☐ | ☐ | ☐ |  | Automate or mechanise the task, especially repetitive functions Modify operation or production method Use bulk handling methods Ensure the equipment accounts for differences in worker size, shape and physical ability – i.e. adjustable or fixed to suit all workers Ensure working heights are matched to the task and the worker Ensure items are within reaching distance Place items where the person can be in a comfortable symmetrical posture when handling Provide seating that matches the needs of the task and the worker – i.e. adjustable seating for multiple workers Alter the size or shape of the load Use power tools Ensure tools are suitable for the task Ensure tools orient the arm, hand and wrist in a power grip position Provide rest breaks and task variation Ensure workloads and deadlines are achievable Allow workers some latitude to influence the rate and pace of work Monitor and control overtime and shiftwork Provide training and supervision |
| Bending or twisting the neck or head forwards, sideways or backwards | ☐ | ☐ | ☐ |  |  |
| Working with one or both hands above shoulder height | ☐ | ☐ | ☐ |  |  |
| Reaching forwards or sideways more than 30cm from the body | ☐ | ☐ | ☐ |  |  |
| Reaching behind the body | ☐ | ☐ | ☐ |  |  |
| Excessive bending of the wrist | ☐ | ☐ | ☐ |  |  |
| Twisting, turning, grabbing, or wringing actions with the fingers, hands or arms | ☐ | ☐ | ☐ |  |  |
| Squatting, kneeling, crawling, lying, semi-lying or jumping | ☐ | ☐ | ☐ |  |  |
| Standing with most of the body’s weight on one leg | ☐ | ☐ | ☐ |  |  |
| Lifting or lowering | ☐ | ☐ | ☐ |  |  |
| Carrying with one hand or one side of the body | ☐ | ☐ | ☐ |  |  |
| Exerting force with one hand or one side of the body | ☐ | ☐ | ☐ |  |  |
| Pushing, pulling and dragging | ☐ | ☐ | ☐ |  |  |
| Very fast actions | ☐ | ☐ | ☐ |  |  |
| Working with the fingers close together or wide apart | ☐ | ☐ | ☐ |  |  |
| Applying uneven, fast or jerky forces | ☐ | ☐ | ☐ |  |  |
| Holding, supporting or restraining anything (including a person, animal or tool) | ☐ | ☐ | ☐ |  |  |

| Duration | Yes | No | N/A | Where ‘yes’ is ticked enter control option/s from Column 6 or enter alternative control/s | Column 6 - Control options. (These are example risk controls and the list is not exhaustive). |
| --- | --- | --- | --- | --- | --- |
| Is the task performed more than 2 hours over a whole shift? | ☐ | ☐ | ☐ |  | Provide rest breaks and task variation Allow workers some latitude to influence the rate and pace of work Monitor and control overtime and shiftwork |
| Is the task performed continually for more than 30 minutes at a time | ☐ | ☐ | ☐ |  |  |

| High or Sudden Forces | Yes | No | N/A | Where ‘yes’ is ticked enter control option/s from Column 6 or enter alternative control/s | Column 6 - Control options. (These are example risk controls and the list is not exhaustive). |
| --- | --- | --- | --- | --- | --- |
| Lifting, lowering or carrying heavy loads | ☐ | ☐ | ☐ |  | Automate or mechanise the task, especially tasks that are repetitive Modify operation or production method Use bulk handling methods Provide a means for attaching mechanical aids for lifting to the load Use jigs to hold or support the items Alter the workplace so mechanical aids can be used and are accessible Reduce weight and dimensions of the load Reduce the number of items handled at one time Provide handles, hand-holds or cut-outs to improve grip Reduce amount of manipulation required (use mechanical aids) Modify the load so mechanical aids can be used Use power tools Ensure tools are suitable for the task Use lightweight tools where possible Use tool counterbalances Ensure tool handles fit workers comfortably Maintain tools and equipment Provide rest breaks and task variation Ensure workloads and deadlines are achievable Allow workers some latitude to influence the rate and pace of work Monitor and control overtime and shiftwork Provide training and supervision |
| Throwing or catching | ☐ | ☐ | ☐ |  |  |
| Hitting or kicking or jumping | ☐ | ☐ | ☐ |  |  |
| Applying a sudden or unexpected force including: Handling a live person or animal or Applying uneven, fast or jerky forces during lifting, carrying, pushing or pulling or Pushing or pulling objects that are hard to move or stop e.g. a trolley | ☐ | ☐ | ☐ |  |  |
| Exerting force while in a bent, twisted or awkward posture including: Supporting items with hands that are above shoulder height or Moving items when legs are in an awkward posture, working with fingers pinched together or held wide apart Using a finger grip or pinch grip or an open handed grip | ☐ | ☐ | ☐ |  |  |
| Exerting a force with the non-preferred hand | ☐ | ☐ | ☐ |  |  |
| Needing to use two hands to operate a tool designed for one hand | ☐ | ☐ | ☐ |  |  |
| The task can only be done for short periods of time | ☐ | ☐ | ☐ |  |  |
| Two or more people need to be assigned to handle a heavy, awkward or bulky load | ☐ | ☐ | ☐ |  |  |
| Workers report pain or significant discomfort during or after the task | ☐ | ☐ | ☐ |  |  |
| Stronger workers assigned to do the task | ☐ | ☐ | ☐ |  |  |
| Workers say the task is physically very strenuous or difficult to do | ☐ | ☐ | ☐ |  |  |
| Workers think the task should be done by more than one person, or seek help to do the task as it requires high force | ☐ | ☐ | ☐ |  |  |