| Safe Work Method Statement (SWMS) Part 1 |
| --- |
| Activity: Plumbing – Gas Fitting | SWMS #: |
| Business Name: Bowley Plumbing Services | ABN: 97 007 937 439 |
| Business Address: 19 Swallow Ave, Modbury Heights SA |
| Business Contact: Phillip Bowley | Phone #: 0418 891 498 |
| SWMS Approved by: Employer / PCBU / Director / OWNER. |
| Name: Phillip Bowley |
| Signature: | Date: |
| Person/s responsible for ensuring compliance with SWMS: Phillip Bowley and all employees |
| Person/s responsible For reviewing the SWMS: Phillip Bowley |
| Relevant workers consulted in the development, approval and communication of this SWMS. | All Persons involved in the task must have this SWMS communicated to them before work commences. |
| Name | Signature | Date | Tool Box Talks will be undertaken to identify, control and communicate additional site hazards. |
| B Small |  |  | Work must cease immediately if incident or near miss occurs. SWMS must be amended in consultation with relevant persons. |
| M Fitch |  |  | Amendments must be approved by Phillip Bowley and communicated to all affected workers before work resumes. |
| T Dawson |  |  | SWMS must be made available for inspection or review as required by WHS legislation. |
|  |  |  | Record of SWMS must be kept as required by WHS legislation (until job is complete or for 2 years if involved in a notifiable incident). |
| Principal Contractor Details (The builder or the organisation you are working for.) |
| Principal Contractor (PC): | Project Name: | Date SWMS provided to PC: |
| Project Address: |
| Project Manager (PM): | PM Signature: | CONTACT PH. #: |
| SWMS Scope: This SWMS covers general safety hazards and risks involved with gas fitting. |

| This work activity involves the following “High Risk Construction Work” |
| --- |
| ☐ Confined Spaces |  Mobile Plant | ☐ Demolition | ☐ Asbestos |
| ☐ Using explosives | ☐ Diving work | ☐ Artificial extremes of temperature | ☐ Tilt up or pre-cast concrete |
|  Pressurised gas distribution mains or piping chemical, fuel or refrigerant lines energised electrical installations or services |
| ☐ Structures or buildings involving structural alterations or repairs that require temporary support to prevent collapse |
|  Involves a risk of a person falling more than 2m, including work on telecommunications towers |
| ☐ Working at depths greater than 1.5 Metres, including tunnels or mines | ☐ Work in an area that may have a contaminated or flammable atmosphere |
| ☐ Work carried out adjacent to a road, railway or shipping lane, traffic corridor | ☐ In or near water or other liquid that involves risk of drowning |
| Likelihood | Insignificant | Minor | Moderate | Major | Catastrophic | Score | Action | HIERARCHY OF CONTROLS | Most Effective |
| Almost certain | 3 High | 3 High | 4 Acute | 4 Acute | 4 Acute |  |  |  |  |
| Likely | 2 Moderate | 3 High | 3 High | 4 Acute | 4 Acute | 4A Acute | DO NOT PROCEED. |  |  |
| Possible | 1 Low | 2 Moderate | 3 High | 4 Acute | 4 Acute | 3H High | Review before commencing work. |  |  |
| Unlikely | 1 Low | 1 Low | 2 Moderate | 3 High | 4 Acute | 2M Moderate | Maintain control measures. |  |  |
| Rare | 1 Low | 1 Low | 2 Moderate | 3 High | 3 High | 1L Low | Record and monitor. |  | Least Effective |
| Personal Protective Equipment (PPE): Ensure all PPE meets relevant Australian Standards. Inspect, and replace PPE as needed. |
| Foot Protection | Hearing Protection | High Visibility | Head Protection | Eye Protection | Face Protection | Hand Protection | Protective Clothing | Breathing Protection | Sun Protection | fall Arrest | Rings, watches, jewellery that may become entangled in machines must not be worn. Long and loose hair must be tied back. |
|  |  |  |  |  |  |  | ☐ |  | ☐ | ☐ |  |
| AS 1319-1994 Safety signs for the occupational environment reproduced with permission from SAI Global under licence 1210-c062. Standards may be purchased at http://www.saiglobal.com |

| Job Step | Potential Hazard/s | IR | Control Measures to Reduce Risk | RR | Responsible Person |
| --- | --- | --- | --- | --- | --- |
| Inherent Risk-rating (IR) Residual Risk-rating (RR) |
| Planning & preparation | Lack of consultation with potential outcomes for personal injury, property damage &/or environmental incident. | 3H | Liaise with Principal Contractor to establish the following on-site systems and procedures are in place and take note of: Health and Safety rules Induction for all workers – site specific and toolbox meetings Supervisory arrangements Emergency plans All relevant workers are appraised for required competencies & for any pre-existing medical conditions if working in remote or isolated locations. Communication arrangements Hazard reporting procedures Injury reporting procedures Ensure Work Safe notification for deep excavations prior for planned work (where applicable) PPE required Site plans – showing no go zones for pedestrians Traffic Management Plan detailing movement of vehicles during work Exclusion Zones Risk Assessments, SWMS and JSA’s Ensure relevant guidance material for electrical NO GO ZONES is on site and consulted before work commences Underground essential services - including gas, water, sewerage, telecommunications, and electricity. Ensure notification of electricity or gas service disruption is given to the site manager / supervisor. Ensure a Confined Space Entry Permit is issued, as required, if work involves a Confined Space. Ensure Hot Work Permits are completed where required. Ensure a working on roofs/heights SWMS is in place (additional to this SWMS) if fitting any appliances e.g. hot water system, to a roof, ceiling space or any other area where the risk of a fall is possible. | 2M |  |
| Training and Capabilities | Lack of training or the assessment of capability may lead to personal injury, property damage &/or environmental incident. | 3H | Ensure all persons entering site have a General Construction Induction Card (white card) Gasfitters are licensed, qualified for and experienced with the type of appliance with which they are working Have registration in the gas-fitting class to which they are working (where applicable) Have appropriate electrical qualifications if undertaking any electrical work e.g. restricted electrical licensing. Gasfitters are able to understand and apply the compliance requirements of the type of gas-fitting work. Ensure all relevant workers have undertaken training and/or received instruction in the use of control measures Include: Instructed on the use of this SWMS Analysing and interpreting design specifications for gas appliances Installing and testing gas appliances Undertaking gas and electrical safety checks, and completing and recording isolation procedures Correct use of equipment inc. selecting, fitting, use, care of & maintenance Emergency plans Use of supervision where required (e.g. new starters or new equipment) Conduct a pre-start toolbox talk to ensure that all workers have been made fully aware of the scope of work to be performed Correct use of all tools used Reporting procedures for incidents Check workers are in fit condition to work i.e. no signs of fatigue, alcohol or drugs. | 2M |  |
| Gas Installation Examples of standards and regulations provided are for example purposes only and may not be applicable to your state or territory. PLEASE CHECK | Lack of compliance with potential outcomes for personal injury, property damage &/or environmental incident. | 3H | Comply with all relevant standards and regulations in force in regards to gas Installation (Set), and installation instructions for connection. Ensure: | 2M |  |
|  |  |  | Correct pipe sizing Meters are not placed in prohibited locations Purging is done with inert gases as required Any pressure changes are within acceptable limits | Location of safety shut off system is compliant Terminated with approved Boundary Control Valve. |  |  |
|  |  |  | Type Name Standard AS/NZS 1596:2014: The storage and handling of LP Gas Standard AS/NZS 5601.1:2013 Gas installations - General installations Regulation Gas Safety (Gas Installation) Regulations 2008 (Victoria) |  |  |
| Assess onsite conditions | Lack of a clear assessment may lead to personal injury, property damage &/or environmental incident. | 3H | Assess conditions at site on arrival. Ensure: Ensure site-specific induction is undertaken (include location of amenities, first aid facilities, emergency plans and evacuation points, incident reporting, communication, contact persons etc.) Assess mobile phone reception (alternative emergency communications procedures in place if no reception available) Work site is exactly as detailed in Terms of Agreement or contract Suitable access for all equipment required Suitable space for operation of equipment Suitable lighting, including night-works. | 2M |  |
|  | Verification of gas supply | 3H | Before commencing an installation, verify: The gas is suitable and safe for the gas appliances and components to be installed, or The appliances and components are suitable to operate on the gas being supplied and comply with local certification requirements. | 2M |  |
|  | Work adjacent to road & public safety | 3H | If setting up roadside – comply with local laws and permits Erect any barriers & signage necessary to keep others safe and aware Ensure reflective vests are worn as required. | 2M |  |
| Work area set up | Muscular stress / musculoskeletal disorder (MSD) | 3H | Movement of material/ from the delivery point to the installation area usually represents the greatest opportunity for damage or injury, particularly if being achieved manually. Ensure: Ensure the access route is clear of hazards Use hand trucks (trolley), to move heavy materials where practicable e.g. hot water systems Use team-lifts where possible: As much as possible, team members are of similar height and capability Team members know their responsibilities during the lift Consider storing the material in a raised position to allow for future access of trolleys or other mechanical aids if required and, to reduce manual handling from ground level. | 2M |  |
|  | Contact with mobile plant | 3H | Check constantly for changing hazards while working and monitor work position at all times Ensure: High visibility clothing worn at all times Do not stand behind reversing vehicles Allow sufficient distance from plant during operation (allow sufficient room for equipment failure – such as arm/boom failure or plant rollover) No work is conducted in established “no go zones” for pedestrians Alertness at all times. Listen for: Reversing alarms/beepers Calls from Plant Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Work positions should be in clear sight of plant operators Follow traffic management plan requirements. Note: Some traffic management plans may say that pedestrians have right-of-way. Never assume this. Make visual and verbal contact with plant operator as required. | 2M |  |
|  | Falls from height > 2m. | 3H | If working at height ensure that suitable fall prevention measures are in place and check that any working platforms can safely support the load. If working at heights above 2m and “in built’ edge protection is not in place or not sufficient ensure a separate, dedicated working at height SWMS is in place before commencing work Additional SWMS may also be required if using Elevating Work Platforms. | 2M |  |
|  | Work adjacent to road & public safety | 3H | Park working vehicle to avoid travelling across roads when delivery working equipment If setting up roadside – comply with local laws and permits Erect any barriers & signage necessary to keep others safe and aware | 2M |  |
|  | Property damage | 3H | Ensure equipment is not placed in areas where they may be run over, damaged or exposed to water (unless rated for wet environments). | 2M |  |
|  | Contact with electricity from existing structure | 4A | Follow lock-out/tag-out procedures and obtain advice from suitable person (such as licensed electrician) that power is isolated (if required). Ensure: Certificate of electrical safety is obtained if required All electrical cables/equipment are identified and marked Fixing points are clear of cables/equipment Where electrical hazards are identified, a qualified electrical contractor should be engaged to eliminate or control this risk. | 2M |  |
|  | Contact with electricity – Power tools | 3H | All power tools and leads are Tested and Tagged and are current Pre-inspect equipment If equipment is damaged, do not use. Take out of service, apply Lock-out/tag-out (LOTO) procedures and inform supervisor immediately. | 2M |  |
|  | Other worker and public safety | 3H | Ensure: | Exclusion zone in place – no unauthorised persons under work Safety Signs Clearly display one or more warning signs that suspended ceiling is being fitted. | 2M |  |
|  | Slips, trips & falls | 3H | Run cords / hoses overhead if possible Place cords / hoses to the side of the walkways and tape down: Avoid running cords / hoses through stairways and ladders Ensure adequate lighting on-site using temporary lighting as required Check your path is clear of obstacles before carrying loads Use mechanical lifting aids rather than carrying bulky loads that block the view ahead Ensure everyone wears suitable footwear with a good grip. | 2M |  |
|  | Noise | 3H | Ensure hearing protection is worn when operating power tools or working with machinery: It is worn by the operator throughout the period of exposure to noise Is suitable for the noise level Is comfortable and correctly fitting for the operator It is regularly inspected and maintained to ensure it remains in good, clean condition. When choosing hearing protection for operators consider: Overprotecting by cutting out too much sound can cause difficulties hearing other sounds needed to work safely Ear-muffs can be uncomfortable to wear in hot environments Wearing PPE can make it difficult for the worker to wear a helmet That long hair can be tied back so it does not impact on correct fit. | 2M |  |
|  | Contact with hazardous chem. / sub. | 3H | Ensure current Material/Safety Data Sheets (M/SDS) are obtained for all hazardous chemicals/substances and accessible on site. | 2M |  |
| Excavation – sub surface installation gas lines | Underground services | 4A | Ensure underground services have been identified and marked accurately for depth and position: Contact Dial Before You Dig (DBYD) 1100 Use accredited cable locator contractor to test the area Contact relevant authorities/companies for ‘as constructed’ plans if necessary Hand excavates using a shovel to locate services and mark out prior to any trenching or battering works Use “Pot holing” techniques if required: Use extreme care when working near gas mains When using hand prodders to locate pipes do not use hammers or other implements Mark all exposed services with flags or devices that can be readily seen Ensure all marked services continue to be visible for the duration of the work. | 2H |  |
|  | Accidental contact (future excavations) | 3H | Ensure marker tape is laid above pipes when installed in an open-cut trench NOTE: The marker tape should be between 150 mm and 300 mm below the finished ground level. | 2M |  |
|  | Gas detection | 4A | Gas detection must be conducted continuously throughout the job Naked flames are prohibited on sites (No Smoking) If a gas main is damaged: Evacuate the immediate area immediately Notify Service Authority Set up an exclusion zone (after advice from Service Authority) Notify Supervisor | 2M |  |
|  | Public access | 3H | Pedestrian Access: Ensure: If closing/modifying a vehicle lane, parking area or footpath the following factors are considered in developing alternative pedestrian access: | 2M |  |
|  |  |  | Travel speed of road traffic Traffic volumes | Percentage of heavy vehicles The alignment of the road |  |  |
|  |  |  | If alternative route is immediately adjacent to the road, concrete or water filled barriers to protect pedestrians from road traffic should be used Pedestrians will be directed by defined walking paths clearly marked with using appropriate measures (e.g. barriers, fencing hazard netting) Signage must be appropriate and easily seen Temporary pathways must have no trip hazards and the ground/pavement should be free of holes, dips, mud or debris Mobility impaired e.g. wheelchair access, pram ramps, hand rails must be considered in respect to widths, surface and grade Barrier fencing or Hoarding must be erected to prevent the public from entering hazardous areas of the work site Access should be monitored through a single entry point. |  |  |
|  | Contact with Mobile plant (excavator etc.) | 3H | Ensure an effective system of communication between machine operator and ground workers is established before work commences Relevant workers must be trained in the procedures involved prior to the work commencing Ground workers are instructed not to approach machine until the operator has agreed to their request to approach Ensure ground workers are instructed on set distances to maintain from the machine while in operation Ground workers are instructed made familiar with the blind spots of the machine. | 2M |  |
|  | Crush injuries | 3H | Never place any part of the body on or near machine while it is in operation Never push another person or engage in horseplay around operating machinery Keep shovels away from trencher chains and augers Always wait for machine to work ahead before cleaning away spoil Do not work within radius of extended booms, near stabilisers or loader buckets. | 2M |  |
| Bottled Gas installation | Fire /explosion – Hazardous atmospheres | 3H | Ensure: Place gas bottles away from electrical devices (any item that can potentially spark) and ignition sources (in the event of a leak) Do not place gas bottles adjacent to wall openings, including windows, doors and vents Maintain a safe distance from openings to below ground spaces, e.g. drains and pits, to prevent possible build-up of the heavier than air gas Gas bottles are placed in well ventilated locations (avoid enclosures) Gas bottles are placed on a solid, well drained base e.g. concrete, pavers Where possible, store cylinders in the shade to avoid exposing cylinders to direct sunlight. Refer to the applicable gas storage standards and regulations for detailed installation requirements (see step 3 of this SWMS) | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Movement of gas cylinders from the delivery point to the installation area usually represents the greatest opportunity for damage or injury, particularly if being achieved manually. Ensure: Ensure the access route is clear of hazards Use hand trucks wherever possible e.g. cylinder trolley with a restraining strap If manual lifting, Use team-lifts where possible: As much as possible, team members are of similar height and capability Team members know their responsibilities during the lift | 2M |  |
|  | Crush injuries | 3H | Keep hands, fingers clear when placing/lifting bottles | Wear steel cap footwear. | 2M |  |
| Hot Tapping | Fire /explosion – Hazardous atmospheres | 4A | Ensure work is planned, coordinated and carried out by persons trained in the procedure Ensure a documented contingency or emergency plan is in place before commencing hot tapping operations. The emergency/contingency plan must cover actions in the event of gas escape, fire or explosion whilst the work is in progress. | 2M |  |
| Running Gas Pipework | Power tools | 3H | Ensure installation manual is available, read and understood Pre-inspect and operate power tools as per manufacturers instructions Ensure equipment rated for atmospheric requirements (water, or explosion-proof for flammable zones) Ensure tool suitable for task: Suited to the material. E.g.: steel, timber MDF, plastic Not too powerful for task. E.g.: don’t use larger drill than needed Sufficient power for task – excessive force not required Safety Devices: Low impact tools where possible Single operation when trigger pressed Guards in place, undamaged, retracts and cover danger areas. Perspex guards not cracked and allow visibility E-stops and other devices functional and tested. | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Ensure equipment is as close to work area as possible There is adequate space to carry out the activity to reduce congestion and manual handling risks Adequate lighting is provided at the work area | Excessively long lengths of pipe are extremely awkward to handle. The larger the diameter of pipe the more the more hazardous it is to handle long lengths Carry lengths of pipe horizontally. | 2M |  |
|  | Cuts /Lacerations | 3H | Use pipe cutters and cable strippers where possible (rather than hacksaws or knives) Opening packaging/bundles: If using knife, always cut away from body Use automatic retracting blade if possible: If not possible, ensure blade is retracted after use | Use caution handling sharp objects Wear gloves when handling offcuts Note location of protruding nails or screws in framing Avoid reaching into areas where you cannot see clearly. | 2M |  |
|  | Dust – Drilling/ cutting masonry or other products that create dust | 3H | Wear eye and breathing protection Local exhaust extraction is provided (if required) Vacuum attachment/bag fitted (if required). Disposable face masks must: Be fitted and used according to manufacturer’s written instructions Fitted tightly. Check the tightness of the headbands and the operation of the one-way valve. (If fitted) Be replaced as required. Facemask life will depend upon amount of air born dust and usage. | 2M |  |
|  | Sub Floor installation | 3H | Check for insects, rodents and reptiles. Engage professional exterminators to clear the area if necessary Seek evaluation from a Hygienist if dust is suspected of being contaminated in any way. Ensure good ventilation of the sub floor area. Use facemasks (P1/P2), safety goggles, and gloves. | 2M |  |
|  | Slips, trips, falls causing injury | 3H | Identify all hazards. Consider: Ground/floor surface condition Where ground surfaces may change level Check design to ensure that the equipment will support a specified load – or ‘duty rating’. This must be clearly stated on the item Sufficient lighting All trip hazards / obstructions removed from work area The work area is not wet under foot | Ensure area is kept clear of packaging, or other debris to prevent tripping/slipping Weather conditions (rain, wind loads, fog, dew) Experience of workers Use pendants, lead stand or insulated cable hangers for power leads Do not drape leads or pipes over body Check for stairs, stored items, corners or other obstructions that could cause tripping. | 2M |  |
|  | Working at elevated positions - Falling objects | 3H | Barricading and signage is developed. Ensure: Signs used to provide clear instruction on entry permissions and hazard areas if working above others Consider appropriate barricades for exclusion zones. Conduct risk assessment and utilise appropriate barricades Consider: Heavy equipment should remain at ground level where possible Maintain good housekeeping, e.g. ensure the work area is tidy and materials, debris, tools and equipment that are not being used are out of the way Providing a secure physical barrier at the edge of the elevated area, i.e. toe boards or infill panels Tethering or otherwise securing tools and materials to prevent them falling on people below Keeping tools or other materials away from edges and off of railings or sills. Remember: If working at heights above 2m and “in built’ edge protection is not in place or not sufficient ensure a separate, dedicated working at height SWMS is in place before commencing work. | 2M |  |
| Fitting appliances / fixtures | Contact with electricity | 4A | Qualified electrician must undertake all electrical hard wiring or installer holds appropriate restricted electrical licence for the work. Where electrical hazards are identified, a qualified electrical contractor should be engaged to eliminate or control this risk. Plugs: Ensure no damage to power cords Do not pinch or trap power cords when installing. | 2M |  |
|  | Contact with gas | 4A | Ensure operating instruction are followed for the installed unit Before connecting to the gas service, purge any debris or air. (Ensure venting of purged gas does not occur where sources of ignition are present). Close the isolating gas cock prior to connection of the appliance Once installation has been completed, pressure test system. | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Avoid awkward and sustained positions Avoid prolonged sitting Use mechanical lifting aids when possible Use two or more people for lifting and moving heavy / awkward equipment Regular breaks For lift from floor level with no lifting aids, ensure safe-lifting techniques used. Example: | 2M |  |
|  |  |  | Plan travel pathway Ensure individual physically ready for lift (muscles warmed up /stretches etc.) Face the load and stand close to load Maintain a wide stance (feet shoulder length apart) Ensure good balance Bend at knees Grip load, ensure firm grip. Keep load close to body | Keep arms and back straight Look forward, and tuck chin into chest Initiate lift using legs muscles Lift smoothly, do not jerk or throw load upwards Avoid any twisting and side-bending during lift When placing load onto ground, follow instructions as above, bend knees, not back |  |  |
|  |  |  | Where Team handling required (as last resort). Ensure: All members of team-lift are matched in size, skills, capabilities Number of persons proportionate to weight of load and level of difficulty Lifts are planned and rehearsed Person allocated to plan and be in charge of lift – all others to know their roles Sufficient space to manoeuvre Use aids where possible (lifting bars, handles etc.) Lifting Aids and equipment: SWL displayed No signs of wear, undamaged Maintained/serviced as required. |  |  |
|  | Using power tools | 3H | Pre-inspect and operate power tools as per manufacturer’s instructions. | 2M |  |
|  | Falls | 3H | Additionally: If working at heights or on a roof and “in built’ edge protection is not in place or not sufficient ensure a separate, dedicated working at heights or, working on a roof SWMS is in place before commencing work. | 2M |  |
|  | Slips, trips | 3H | Electrical leads to be kept as short as possible and will be located where they will not provide a tripping hazard or be exposed to damage | Tape leads across doorways/walkways Excess lengths will be located along a wall or partition Clean up spills, leaks immediately. | 2M |  |
|  | Caulking/sealants | 3H | Follow directions of use Consult M/SDS for the product Ensure adequate ventilation | Dispose of chemicals correctly Wash your hands thoroughly after handling chemicals Chemical resistant gloves for prolonged exposure. | 2M |  |
| Purging gas lines | Contact with Gas | 3H | Purge all air or inert gas (using inert gases) from piping before anyone lights a gas appliance. All branch lines must be individually purged: | 2M |  |
|  |  |  | Purge. Stop. | Tighten fitting. Wait and let air dissipate before lighting. |  |  |
|  |  |  | Ensure all sources of ignition, where natural gas may be vented, are identified and eliminated Purging should only be done in a well-ventilated area or by safely venting the contents into the outside atmosphere where there are no people, structures or sources of ignition Do not purge contents into a confined space or where gas can accumulate Use gas detection equipment during all gas release operations to prevent gas from accumulating. |  |  |
| Commission appliances | Contact with gas | 3H | All piping to be pressure tested after the installation and before being place in operation to demonstrate it has adequate strength and does not leak. Conduct pressure testing as per applicable gas storage standards and regulations Follow manufacturer’s instructions Check ignition of each burner of the appliance | Test all safety devices for correct operation Explain to client, when present, how to safely and correctly operate the appliance and any other equipment necessary (Ensure the client receives the operating instructions. | 2M |  |
| On completion | Slips, trips, falls causing injury | 3H | Site to be left in clean and tidy condition ready for handover. Builder / supervisor to be advised upon completion of works. | 2M |  |
|  | Compliance | 3H | Supply client with a copy of an installation certificate and/or fix a compliance plate or badge to the installation. | 2M |  |
|  | Environmental incident | 3H | Dispose of all hazardous chemicals/sealants in an approved waste receptacle. | 2M |  |
|  | Contact with electricity | 4A | Ensure that no electrical appliances, light fittings, cables etc. have been damaged during installation If damage suspected, do not turn power back on – seek advice from licensed electrician. | 2M |  |
|  | Contact with hazardous materials | 3H | Clean debris and ensure off cuts are removed from area Observe good personal hygiene including washing hands before eating. | 2M |  |
|  | Public safety | 3H | If acceptable, remove barricades, contact supervisor and return as agreed Final visual inspection before leaving area. | 2M |  |

| Emergency Response - Call 000 immediately. |
| --- |
| If work is to be conducted on a construction site (or a site controlled by another Employer / PCBU) follow the site-specific Emergency Management Plan. Ensure: Adequate numbers of first aid trained staff are on site when working at heights occurs First aiders are trained and competent in managing injuries associated with demolition until emergency services arrive All rescue equipment is in good condition, available for use and in close proximity to the work site. | Ensure workers have access to: First aid kit/supplies First Aid trained personnel familiar with Resuscitation and emergency response for electric shock M/SDS Communication devices (check mobile phones will have service in area) Suitable fire protection equipment. |
| Safe Work Method Statement (SWMS) Part 2 |
| Formal Training, Licences required for workers undertaking this task: | Relevant Legislation & Codes of Practice Retain only the legislation references applicable to your state of operation for this SWMS. |
| Delete or add as relevant Licence to Perform High Risk Work (operating certain plant, equipment) TAFE or other recognised training organisation Construction Induction Card (or equivalent) Competent in operation of make/model of plant Emergency procedures – emergency response PPE Traffic Management Plans | Commonwealth, NSW, QLD, ACT Work Health and Safety Act 2011 Work Health and Safety Regulations 2011 Northern Territory Work Health and Safety (National Uniform Legislation) Act 2011 Work Health and Safety (National Uniform Legislation) Regulations SA, Tasmania Work Health and Safety Act 2012 Work Health and Safety Regulations 2012 Codes of Practice: Safe Work Australia (2011): Construction Work First Aid in the Workplace Managing the Risk of Falls at Workplaces Managing the Risk of Plant in the Workplace Managing Noise and Preventing Hearing Loss in the Workplace How to Manage Work Health and Safety Risks Hazardous Manual Tasks Managing Risks of Hazardous Chemicals Managing Electrical Risks in the Workplace Managing the Work Environment and Facilities WHS Consultation, Cooperation & Coordination | Victoria: Occupational Health & Safety Act 2004 Occupational Health & Safety Regulations 2007 Compliance Codes: WorkSafe Victoria (2008): Compliance Code: Communicating OHS Across Languages First Aid in the Workplace Prevention of Falls in General Construction Workplace Amenities and Work Environment Codes of Practice: WorkSafe Victoria (1990): No. 13: Building and Construction Workplaces (2000): No. 25: Manual Handling (1995): No. 19: Plant (1998): No. 23: Plant (Amendment No. 1) (2004): No. 29: Prevention of Falls in Housing Construction (2000): No. 24: Hazardous Substances Western Australia Occupational Safety & Health Act 1984 Occupational Safety & Health Regulations 1996 Codes of Practice: |
| Details of Supervisory Arrangements for workers undertaking this task: |  |  |
| Delete or add as relevant Suitably qualified supervisors for job Direct on-site supervision Remote site – communication systems/ schedule Audits Spot Checks, etc. Reporting systems |  |  |
| Details of: regulatory permits/licenses Engineering Details/Certificates/WorkCover. Approvals: |  |  |
| Delete or add as relevant Local council permits Authorisation to work Confined Space Permit Building Approvals EPA approvals/permits Certain plant to be registered with State Authority PPE to comply with relevant Australian Standards |  |  |
|  | Plant/Tools/Equipment List for the job. | Reference Documents |
|  | (Make & Model) |  |

| Safe Work Method Statement (SWMS) Part 3 |
| --- |
| This SWMS has been developed in consultation and cooperation with employee/workers and relevant Employer/Persons Conducting Business or Undertaking (PCBU). I have read the above SWMS and I understand its contents. I confirm that I have the skills and training, including relevant certification to conduct the task as described. I agree to comply with safety requirements within this SWMS including risk control measures, safe work instructions and Personal Protective Equipment described. |
| Overall Risk Rating after Controls | 1 Low | 2 Moderate | 3 High | 4 Acute |
| Employee/Worker Name | Job Role / Position | Signature | Date | Time | Employer/PCBU/ Supervisor |

| Review: Ensure all controls are reviewed as per the following: If controls fail to reduce risk adequately When changes to the workplace or work activity occur that create new / different risks where controls may no longer be effective New hazards identified After an incident involving work activities relevant to this SWMS During consultation with relevant persons indicate review is needed A Health and Safety Representative (HSR) requests a review in line with the requirements of the legislation. | Monitor: To ensure controls are implemented and monitored effectively: Toolbox /pre-work meetings will be undertaken Relevant persons will be consulted on hazards and contents of SWMS, work plans and other applicable information Control measures will be monitored throughout works: *Spot checks *Consultation *Scheduled audits Corrective actions will be recorded and rectified in a timely manner SWMS will be reviewed and updated accordingly (in consultation with relevant persons). |
| --- | --- |
| Review No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Name: |  |  |  |  |  |  |  |  |  |  |
| Initial: |  |  |  |  |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |  |  |  |  |