| Safe Work Method Statement (SWMS) Part 1 |
| --- |
| Activity: Pump & Valve Installation | SWMS #: |
| Business Name: Bowley Plumbing Services | ABN: 97 007 937 439 |
| Business Address: 19 Swallow Ave, Modbury Heights SA |
| Business Contact: Phillip Bowley | Phone #: 0418 891 498 |
| SWMS Approved by: Employer / PCBU / Director / OWNER. |
| Name: Phillip Bowley |
| Signature: | Date: |
| Person/s responsible for ensuring compliance with SWMS: Phillip Bowley and all employees |
| Person/s responsible For reviewing the SWMS: Phillip Bowley |
| Relevant workers consulted in the development, approval and communication of this SWMS. | All Persons involved in the task must have this SWMS communicated to them before work commences. |
| Name | Signature | Date | Tool Box Talks will be undertaken to identify, control and communicate additional site hazards. |
| B Small |  |  | Work must cease immediately if incident or near miss occurs. SWMS must be amended in consultation with relevant persons. |
| M Fitch |  |  | Amendments must be approved by Phillip Bowley and communicated to all affected workers before work resumes. |
| T Dawson |  |  | SWMS must be made available for inspection or review as required by WHS legislation. |
|  |  |  | Record of SWMS must be kept as required by WHS legislation (until job is complete or for 2 years if involved in a notifiable incident). |
| Principal Contractor Details (The builder or the organisation you are working for.) |
| Principal Contractor (PC): | Project Name: | Date SWMS provided to PC: |
| Project Address: |
| Project Manager (PM): | PM Signature: | CONTACT PH. #: |
| SWMS Scope: This SWMS covers the removal and installation of industrial pumps and valves. Covered in this SWMS is the loading/unloading of materials and equipment, work area set up, manual handling, lifting by crane or machinery, and testing of new installations. This SWMS is also suitable for the installation of fire service booster assemblies and hydrants. (This SWMS does not include controls for the use of any mobile plant, confined space operations or working at heights over 2m. Separate dedicated SWMS will be required for these tasks.) |

| This work activity involves the following “High Risk Construction Work” |
| --- |
| ☐ Confined Spaces |  Mobile Plant | ☐ Demolition |  Asbestos |
| ☐ Using explosives | ☐ Diving work | ☐ Artificial extremes of temperature | ☐ Tilt up or pre-cast concrete |
|  Pressurised gas distribution mains or piping chemical, fuel or refrigerant lines energised electrical installations or services |
| ☐ Structures or buildings involving structural alterations or repairs that require temporary support to prevent collapse |
| ☐ Involves a risk of a person falling more than 2m, including work on telecommunications towers |
| ☐ Working at depths greater than 1.5 Metres, including tunnels or mines | ☐ Work in an area that may have a contaminated or flammable atmosphere |
| ☐ Work carried out adjacent to a road, railway or shipping lane, traffic corridor |  In or near water or other liquid that involves risk of drowning |
| Likelihood | Insignificant | Minor | Moderate | Major | Catastrophic | Score | Action | HIERARCHY OF CONTROLS | Most Effective |
| Almost certain | 3 High | 3 High | 4 Acute | 4 Acute | 4 Acute |  |  |  |  |
| Likely | 2 Moderate | 3 High | 3 High | 4 Acute | 4 Acute | 4A Acute | DO NOT PROCEED. |  |  |
| Possible | 1 Low | 2 Moderate | 3 High | 4 Acute | 4 Acute | 3H High | Review before commencing work. |  |  |
| Unlikely | 1 Low | 1 Low | 2 Moderate | 3 High | 4 Acute | 2M Moderate | Maintain control measures. |  |  |
| Rare | 1 Low | 1 Low | 2 Moderate | 3 High | 3 High | 1L Low | Record and monitor. |  | Least Effective |
| Personal Protective Equipment (PPE): Ensure all PPE meets relevant Australian Standards. Inspect, and replace PPE as needed. |
| Foot Protection | Hearing Protection | High Visibility | Head Protection | Eye Protection | Face Protection | Hand Protection | Protective Clothing | Breathing Protection | Sun Protection | fall Arrest | Rings, watches, jewellery that may become entangled in machines must not be worn. Long and loose hair must be tied back. |
|  |  | ☐ |  |  | ☐ |  | ☐ |  | ☐ |  |  |
| AS 1319-1994 Safety signs for the occupational environment reproduced with permission from SAI Global under licence 1210-c062. Standards may be purchased at http://www.saiglobal.com |

| Job Step | Potential Hazard/s | IR | Control Measures to Reduce Risk | RR | Responsible Person |
| --- | --- | --- | --- | --- | --- |
| Inherent Risk-rating (IR) Residual Risk-rating (RR) |
| Planning & preparation | Lack of consultation with potential outcomes for personal injury, property damage &/or environmental incident. | 3H | Liaise with Principal Contractor to establish the following on-site systems and procedures are in place and take note of: Health and Safety rules Induction for all workers – site specific and toolbox meetings Supervisory arrangements Communication arrangements All relevant workers are appraised for required competencies & for any pre-existing medical conditions if working in remote or isolated locations. PPE required Site plans – showing no go zones for pedestrians Traffic Management Plan Exclusion Zones Risk Assessments SWMS and JSA’s Injury reporting procedures Hazard reporting procedures. | 2M |  |
|  | Atmospheric hazard - poor air quality/ chemical exposures | 4A | Note: A confined space can be defined as an enclosed or partially enclosed space that is likely to be a risk to health and safety because of: An atmosphere that does not have a safe oxygen level, or Contaminants, including airborne gases, vapours and dusts, that may cause injury from fire or explosion, or Harmful concentrations of any airborne contaminants. If work involves an identified Confined Space, a separate, dedicated ‘Confined Spaces SWMS’ is required to be used in conjunction with this SWMS. Examples of confined spaces involved with installing insulation batts might include ceilings or wall cavities, when these examples meet the definition of a confined space Ensure a confined space entry permit is issued for each confined space entry. | 2M |  |
|  | Personal Injury from delay in emergency assistance to remote workers | 3H | A ‘Buddy’ system is utilised for high-risk tasks undertaken in remote locations or working in isolation. A procedure is developed and in place for regular contact with people working remotely or in isolation, The procedure should identify: Travel itineraries, locations, scheduled contact persons and times Sufficient supplies of water, food, fuel & supplies needed An emergency response Appropriate Vehicles Safety equipment including first aid. | 2M |  |
| Training and Capabilities | Lack of training or the assessment of capability may lead to personal injury, property damage &/or environmental incident. | 3H | Check workers are in fit condition to work i.e. no signs of fatigue, alcohol or drugs. If working on EWPs or scaffolding, or operating mobile plant for this task, ensure there are separate, dedicated SWMS in place and that all workers/employees have relevant training and licensing. Ensure all persons entering a construction site have a General Construction Induction Card (white card) Ensure relevant workers/employees have appropriate licences for operation Ensure all relevant workers have undertaken training and/or received instruction in the use of control measures. Include: | 2M |  |
|  |  |  | Follow all installation instructions Reporting procedures for incidents Correct use of equipment including selecting, fitting, use, care of and maintenance Correct use of all tools used Correct use of height access equipment | Installed as per regulated authority requirements Use of supervision where required (e.g. new starters or new equipment) Ensure supervisors, foremen etc. are suitably experienced in the type work to be conducted All workers are trained in this SWMS. |  |  |
| Assess onsite conditions | Lack of a clear assessment may lead to personal injury, property damage &/or environmental incident. | 3H | Assess conditions at site on arrival. Ensure: Ensure site-specific induction is undertaken (amenities, first aid facilities, emergency plans and evacuation points, incident reporting, communication, contact persons etc.) Assess mobile phone reception (alternative emergency communications procedures in place if no reception available) Work site is exactly as detailed in Terms of Agreement or contract Suitable access for all equipment required Suitable space for operation of equipment Suitable lighting, including night-works Conduct risk assessment to identify potential hazards such as: | 2M |  |
|  |  |  | Lighting Ventilation Dust Work at heights (> 2m) Temperature etc. Presence of hazardous materials such as asbestos, lead, silica etc. | Location of existing services (heating, water, pipes, electrical leads) Exposed electrical switchboards/power points Duration of manual handling tasks (such as working with arms above shoulder height). Load bearing capacity of support structures. |  |  |
| Delivery of materials and equipment (Pumps, Valves etc) | Hit by mobile plant/vehicle | 3H | Alertness at all times. Listen for: Reversing alarms/beepers Calls from Plant Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Reversing trucks, ensure: Never stand between truck and another structure when vehicle is reversing Always maintain visual contact with driver’s mirrors (Remember: if you can’t see the driver – he can’t see you!) Use a spotter where practicable to direct trucks on site When unloading ensure: Within Safe working load (SWL) if using hoisting machinery Suitable ground and sufficient room for operation Delivery driver and other personnel are removed from area (use physical barriers to maintain exclusion zone). | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Where possible, pumps/motors and associated material should be unloaded using mechanical means. E.g. forklift, truck crane etc. Where manual unloading and storage is undertaken: Ensure the access route is clear of hazards Use hand trucks (sheet trolley), to move heavy items where practicable Use team-lifts where possible As much as possible, team members are of similar height and capability Team members know their responsibilities during the lift Ensure materials /equipment is stored as close to work area as possible The floor loading design of the building or platform should be carefully considered and, if necessary, the material evenly distributed Consider storing the material in a raised position e.g. on dunnage to allow for future access of trolleys/other mechanical aids if required & to reduce manual handling from ground level. | 2M |  |
| Work area set up | Muscular stress / musculoskeletal disorder (MSD) | 3H | Use hand trucks, to move heavy materials Use team-lifts for heavier equipment Ensure materials / equipment is as close to work area as possible. | 2M |  |
|  | Work adjacent to road & public safety | 3H | Park working vehicle to avoid travelling across roads when delivery working equipment If setting up roadside – comply with local laws and permits Erect any barriers & signage necessary to keep others safe and aware. | 2M |  |
|  | Property damage | 3H | Ensure equipment is not placed in areas where they may be run over, damaged or exposed to weather. Keep power leads up off the ground and out of the way. | 2M |  |
|  | Safety of public during work process | 3H | During installation work, ensure: Relevant persons notified of type of works and expected duration Relevant persons are informed of LOTO procedures (that power must not be returned to areas that have been isolated with locks/dangers tags in place) Barricades in place to prevent unauthorized entry to work area Signage in place to caution persons not to enter. | 2M |  |
|  | Environmental noise | 3H | All noisy construction work conducted within regulated hours (see local council / EPA for details) Be aware of noise impacts at all times of day and take reasonable steps to reduce noise. | 2M |  |
|  | Contact with electricity from existing structure | 4A | Ensure all power to electrical cables is isolated before work commences Follow lock-out/tag-out procedures and obtain advice from suitable person (such as licensed electrician) that power is isolated (if required). Liaise with other contractors on site (such as electricians) to ensure their work will not create hazards during installation Electrical leads are not on the floor or in contact with wet surfaces. | 2M |  |
|  | Power tools | 3H | Ensure operations manual is available, read and understood Pre-inspect and operate power tools as per manufacturers instructions Ensure equipment rated for atmospheric requirements (water, or explosion-proof for flammable zones) Ensure tool suitable for task: Suited to the material. E.g.: steel, timber MDF, plastic Not too powerful for task. E.g.: don’t use larger drill than needed Sufficient power for task – excessive force not required Safety Devices: Low impact tools where possible Single operation when trigger pressed Guards in place, undamaged, retracts and cover danger areas. Perspex guards not cracked and allow visibility E-stops and other devices functional and tested. | 2M |  |
|  | Contact with mobile plant or passing vehicle | 3H | Check constantly for changing hazards while working and monitor work position at all times. Ensure: | 2M |  |
|  |  |  | High visibility clothing worn at all times Do not stand behind reversing vehicles Allow sufficient distance from plant during operation (allow sufficient room for equipment failure – such as arm/boom failure or plant rollover) No work is conducted in established “no go zones” for pedestrians | Alertness at all times. Listen for: Reversing alarms/beepers Calls from Plant Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Work positions should be in clear sight of plant operators Follow traffic management plan requirements. |  |  |
|  |  |  | NOTE: Some traffic management plans may say that pedestrians have right-of-way. Never assume this. Make visual and verbal contact with plant operator as required. |  |  |
|  | Slips, trips & falls on the same level | 3H | Work area (particularly floor surfaces) is in safe condition to avoid trips | Electrical leads are not on the floor The work area is not wet under foot Free of clutter. | 2M |  |
|  | Hazardous Materials - Asbestos | 3H | Ensure as much information as possible is obtained on location and condition of any asbestos containing material (ACM) in the area to be worked on. If removing, fixing to or drilling into asbestos-containing materials, ensure a separate, dedicated Asbestos (working with) SWMS is in place and used for the task. | 2M |  |
| Hot Works | Property damage | 3H | Ensure suitable Hot Works Permit obtained for any hot work activities (including welding). Include, at least: | 2M |  |
|  |  |  | Exact details of job (location, time/date, equipment to be used, name of all workers etc.) Permit for each day required Fire protection equipment available Follow safety precautions on Hot Work Permit | Do not conduct work that is not listed on Hot Work Permit If other Hot Works are required, obtain Hot Work Permit for that task before commencement Use Spotter as required. |  |  |
|  | Burns | 3H | Ensure appropriate PPE (cotton clothing, leather or welding type gloves, goggles with side shields or welding mask with filter lens as required). Ensure Operator does not have matches or a lighter on them Avoid clothing that has the potential to capture hot sparks and metal debris, e.g. pockets or other folds Mark or label as ‘hot’ equipment, metals, plates or items likely to be hot in the welding area to minimise accidental burns Picking up debris – use gloves. | 2M |  |
| Disconnecting an existing pump/motor/valve. | Contact with electricity | 4A | Ensure all power to electrical cables is isolated before work commences Follow lock-out/tag-out procedures and obtain advice from suitable person (such as licensed electrician) that power is isolated (if required). Liaise with other contractors on site (such as electricians) to ensure their work will not create hazards during installation Electrical leads are not on the floor or in contact with wet surfaces. | 2M |  |
|  | Hit by objects/ fluids under pressure | 4A | Liaise with site management (or controller of pipe work to arrange for suitable Lock-out/Tag-out (LOTO) procedures. Include (at least): | 2M |  |
|  |  |  | Confirmation of locking sites from drawings /plans and instructions from suitable competent persons /manufacturer) Draining of relevant pipes (pressure & substances) Purging /cleaning relevant pipes to ensure no hazardous chemicals are present during installation works Locking of all valves to prevent inflow of hazardous chemicals, sewerage or water (or any other substance) Suitable locks and tags System in place to monitor locks/tags and any unauthorized removal Verification that system is clean (atmospheric testing) isolated and locked out. | Only suitably qualified and trained personnel conduct operations or fully supervise others with less experience Relieve pressure on pump/valves as required (pressure relief valves, plugs etc.) Isolate and disconnect hydraulic hoses if applicable (ensure hoses are restrained or anchored prior before attempting to remove) Remove all other fittings as necessary. Remove hold down bolts. Ensure pump/valve is completely disconnected and free to move. |  |  |
|  | Slips, trips and falls | 3H | Remove pipefittings ensuring any residual fluid is drained away safely with consideration of fluid type and where it will drain. If unexpected fluids or odours are detected during this process retighten if possible or stop and leave the area immediately if unsure. (Investigate before continuing). | 2M |  |
| Lifting Pumps- Motors-Valves into/out of position | Contact with electricity | 4A | Ensure work is not conducted in close proximity to electrical power lines or other electrical installations. Check for: | 2M |  |
|  |  |  | Overhead power lines (including high and low voltage distribution conductors) Single wire earth return (SWER) Service cables to premises | Communications cables Electrical transformers (mounted lower than cables) |  |  |
|  |  |  | Identify maximum range of equipment and how close equipment or load can come to asset (known as design envelope). The following dimensions are taken from the closest point of any extended component of the machine e.g. extended long reach boom. Approach distances will vary based on the voltage level of the live electrical Apparatus. Always contact your local power asset owner for information prior to commencing crane operations if unsure. |  |  |
|  | Hit by falling objects | 3H | The pump/motor/valve should be unloaded by means of a crane or other suitable lifting device of sufficient capacity (ensure licenced rigger or dogman used) Only use lifting mechanisms, crane, chain pulleys, etc. of adequate capacity. Machinery to lift and place pump: Ensure pump/motor is secured to prevent movement before releasing any connections or hold downs (If pump is to be lifted or lowered ensure all slings or other equipment is securely fastened beforehand) Ensure that the plant and equipment will operate within their safe working load limits Check: Weight of load – this should be marked on the load Uniformity of the load – identify the centre of gravity to limit any possible load swinging That the location where the load is to be placed is clear of obstructions. This includes overhead obstructions such as power lines as well as surface or trench obstructions Lifting gear should be checked before and after use, and inspected regularly to determine whether it is suitable to keep using | 2M |  |
|  |  |  | Load travel: | Keep the load stable and under control at all times Use one or more taglines to prevent uncontrolled motion Taglines attached must be 16mm diameter rope |  |  |
|  |  |  | Never work under a suspended load Avoiding lifting or swinging the load over workers below Never wrap the hoist rope around the load Only travel with load attached if the crane is designed to do this Keep the load as low as possible. |  |  |
|  | Public safety | 3H | Exclusion Zones must be established to stop people entering the area and being injured by the crane or falling objects Barricades in place to prevent unauthorised entry to work area if necessary Signage in place to caution persons not to enter Spotter used where risk of public entry is high. | 2M |  |
|  | Property damage | 3H | Ensure slings and other equipment is not placed in areas where it may be run over, damaged or exposed to water (unless rated for wet environments) Plan setup location to avoid contact with structures. | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD | 3H | Small pumps/motors/valves that do not require mechanical assistance to lift. Ensure safe-lifting techniques used. Example: Plan travel pathway Ensure individual physically ready for lift (muscles warmed up /stretches etc.) Face the load and stand close to load Lift smoothly, do not jerk or throw load upwards Avoid any twisting and side-bending during lift When placing load onto ground, follow instructions as above, bend knees, not back Avoid long periods of repetitive movements: Avoid awkward and sustained positions Use two or more people for lifting and moving heavy / awkward items Take Regular breaks. | 2M |  |
| Gasket removal/ Flange cleaning | Cuts /lacerations | 3H | Clean old joint flange faces: | Use caution scraping old gasket material off Always scrap away from body Do not use excessive force. | 2M |  |
|  | Contact with hazardous chemicals / substances | 3H | Ensure current Material/Safety Data Sheets (M/SDS) are available for all hazardous chemicals/substances and accessible on site i.e. gasket strippers Containers are labelled (name of product and safety information) Appropriate containers/spray bottles are used: Only use chemicals/substances as per the label instructions | Never use food/drink containers for storing / decanting chemicals Do not breathe dust / fume / gas / mist / vapours / spray Wash hands thoroughly after handling Do not eat, drink or smoke when using these products Use only a well-ventilated area Wear protective gloves/protective clothing/eye protection/face protection. | 2M |  |
|  | Fire /Explosion | 4A | Most gasket removers are flammable Keep away from heat/sparks/open flames | DO NOT smoke Ensure fire extinguisher on hand. | 2M |  |
| Replace/ fit new pump /motor/valve | Contact with electricity | 3H | Ensure only suitably qualified electricians (or those with appropriate restricted electrical licences) install all electrical installations associated with the pump unit. | 2M |  |
|  | Hit by objects/ fluids under pressure | 3H | Before installation, all fittings should be thoroughly inspected for flaws created during manufacture, shipping or unloading of the pump or other components Install as per manufacturer’s instructions and regulations Confirmation drawings /plans and instructions from suitable competent persons /manufacturer). After installation: | 2A |  |
|  |  |  | Remove locks and tags from isolation valves Unlock isolation valves to new fixture Verification that system is clean (atmospheric testing) isolated and free of leaks or failures | Only suitably qualified and trained personnel conduct installation or fully supervise others with less experience Slowly increase pressure on pump/valves as required (System in place to monitor system after fluids are allowed to enter system. |  |  |
|  | Pressure testing pipe work / Hit by objects under pressure | 4A | Testing new system: Only competent person to perform the pressure testing task. All unnecessary personnel cleared from area before testing commences Ensure all connections are adequately secured The test pressure applied should not exceed: Designed maximum operating pressures Designed pressure rating of any system component, whichever is lowest. | 2M |  |
| Working at elevated levels | Falls from trestles | 3H | Be rated for proposed weight and span Have an overhang of at least 150 mm and not more than 250mm at each end and be “locked” together. Example - clamped near the centre span to prevent individual movement Have an unobstructed surface width of at least 450mm (two planks wide) Must be matched pairs i.e. the rungs should be equivalent heights and spacing. | 2M |  |
|  | Fall from ladder | 3H | Work positioning. Ensure: Load rating of at least 120kg Correct size and length for job No damage, clean and dry Secured to work site (base and top) Metallic, wire- reinforced or conductive ladders should be avoided around live electrical equipment Face ladder when ascending/descending. Ensure 3 points of contact remain on ladder at all times Ensure only 1 person working from each ladder. | 2M |  |
|  | Falls from platform ladders | 3H | Ensure | Trestle back undamaged If unfolding type, chains, rivets etc. are undamaged and functional Suitable height hand rail (900mm) Triangular flat plate bracing Correct size for job (platform level) | Non-slip treads Large feet with non-slip mouldings Non-slip platform of sufficient strength for persons, tools and equipment Industrial rating. | 2M |  |
| On completion | Slips, trips, falls causing injury | 3H | Clean debris and ensure larger cut-offs are removed from area | Clean up tools and any waste Site to be left in clean and tidy condition. | 2M |  |
|  | Contact with electricity | 4A | Ensure that no electrical appliances, cables etc. have been damaged during installation. Disconnect power tool/extension leads from power point before winding up, so that you don’t get a shock if the lead is damaged Inspect leads and power equipment for damage If safe to do so, remove isolation locks/tags and test for function. | 2M |  |
|  | Contamination of waterways and water catchment | 3H | Dispose of off-cut materials in approved waste containers Dispose of empty containers / bags in approved waste containers Do not wash out tools or containers where residue can enter waterways or drains. Use spill kit where required for waste fluids. | 2M |  |
|  | Public safety | 3H | If acceptable, remove barricades, contact supervisor and return as agreed. | 2M |  |

| Emergency Response - Call 000 immediately. |
| --- |
| If work is to be conducted on a construction site (or a site controlled by another Employer / PCBU) follow the site-specific Emergency Management Plan. Ensure: Adequate numbers of first aid trained staff are on site when working at heights occurs First aiders are trained and competent in managing injuries associated with demolition until emergency services arrive All rescue equipment is in good condition, available for use and in close proximity to the work site. | Ensure workers have access to: First aid kit/supplies First Aid trained personnel familiar with Resuscitation and emergency response for electric shock M/SDS Communication devices (check mobile phones will have service in area) Suitable fire protection equipment. |
| Safe Work Method Statement (SWMS) Part 2 |
| Formal Training, Licences required for workers undertaking this task: | Relevant Legislation & Codes of Practice Retain only the legislation references applicable to your state of operation for this SWMS. |
| Delete or add as relevant Licence to Perform High Risk Work (operating certain plant, equipment) TAFE or other recognised training organisation Construction Induction Card (or equivalent) Competent in operation of make/model of plant Emergency procedures – emergency response PPE Traffic Management Plans | Commonwealth, NSW, QLD, ACT Work Health and Safety Act 2011 Work Health and Safety Regulations 2011 Northern Territory Work Health and Safety (National Uniform Legislation) Act 2011 Work Health and Safety (National Uniform Legislation) Regulations SA, Tasmania Work Health and Safety Act 2012 Work Health and Safety Regulations 2012 Codes of Practice: Safe Work Australia (2011): Construction Work First Aid in the Workplace Managing the Risk of Falls at Workplaces Managing the Risk of Plant in the Workplace Managing Noise and Preventing Hearing Loss in the Workplace How to Manage Work Health and Safety Risks Hazardous Manual Tasks Managing Risks of Hazardous Chemicals Managing Electrical Risks in the Workplace Managing the Work Environment and Facilities WHS Consultation, Cooperation & Coordination | Victoria: Occupational Health & Safety Act 2004 Occupational Health & Safety Regulations 2007 Compliance Codes: WorkSafe Victoria (2008): Compliance Code: Communicating OHS Across Languages First Aid in the Workplace Prevention of Falls in General Construction Workplace Amenities and Work Environment Codes of Practice: WorkSafe Victoria (1990): No. 13: Building and Construction Workplaces (2000): No. 25: Manual Handling (1995): No. 19: Plant (1998): No. 23: Plant (Amendment No. 1) (2004): No. 29: Prevention of Falls in Housing Construction (2000): No. 24: Hazardous Substances Western Australia Occupational Safety & Health Act 1984 Occupational Safety & Health Regulations 1996 Codes of Practice: |
| Details of Supervisory Arrangements for workers undertaking this task: |  |  |
| Delete or add as relevant Suitably qualified supervisors for job Direct on-site supervision Remote site – communication systems/ schedule Audits Spot Checks, etc. Reporting systems |  |  |
| Details of: regulatory permits/licenses Engineering Details/Certificates/WorkCover. Approvals: |  |  |
| Delete or add as relevant Local council permits Authorisation to work Confined Space Permit Building Approvals EPA approvals/permits Certain plant to be registered with State Authority PPE to comply with relevant Australian Standards |  |  |
|  | Plant/Tools/Equipment List for the job. | Reference Documents |
|  | (Make & Model) |  |

| Safe Work Method Statement (SWMS) Part 3 |
| --- |
| This SWMS has been developed in consultation and cooperation with employee/workers and relevant Employer/Persons Conducting Business or Undertaking (PCBU). I have read the above SWMS and I understand its contents. I confirm that I have the skills and training, including relevant certification to conduct the task as described. I agree to comply with safety requirements within this SWMS including risk control measures, safe work instructions and Personal Protective Equipment described. |
| Overall Risk Rating after Controls | 1 Low | 2 Moderate | 3 High | 4 Acute |
| Employee/Worker Name | Job Role / Position | Signature | Date | Time | Employer/PCBU/ Supervisor |

| Review: Ensure all controls are reviewed as per the following: If controls fail to reduce risk adequately When changes to the workplace or work activity occur that create new / different risks where controls may no longer be effective New hazards identified After an incident involving work activities relevant to this SWMS During consultation with relevant persons indicate review is needed A Health and Safety Representative (HSR) requests a review in line with the requirements of the legislation. | Monitor: To ensure controls are implemented and monitored effectively: Toolbox /pre-work meetings will be undertaken Relevant persons will be consulted on hazards and contents of SWMS, work plans and other applicable information Control measures will be monitored throughout works: *Spot checks *Consultation *Scheduled audits Corrective actions will be recorded and rectified in a timely manner SWMS will be reviewed and updated accordingly (in consultation with relevant persons). |
| --- | --- |
| Review No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Name: |  |  |  |  |  |  |  |  |  |  |
| Initial: |  |  |  |  |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |  |  |  |  |

# Text boxes

DO NOT:

- Attempt to move or extend ladder when on it

- Slide down stiles

- Step up or down two or more rungs at a time