| Safe Work Method Statement (SWMS) Part 1 |
| --- |
| Activity: Plumbing - Truck Mounted Hydro-Jetting | SWMS #: |
| Business Name: Bowley Plumbing Services | ABN: 97 007 937 439 |
| Business Address: 19 Swallow Ave, Modbury Heights SA |
| Business Contact: Phillip Bowley | Phone #: 0418 891 498 |
| SWMS Approved by: Employer / PCBU / Director / OWNER. |
| Name: Phillip Bowley |
| Signature: | Date: |
| Person/s responsible for ensuring compliance with SWMS: Phillip Bowley and all employees |
| Person/s responsible For reviewing the SWMS: Phillip Bowley |
| Relevant workers consulted in the development, approval and communication of this SWMS. | All Persons involved in the task must have this SWMS communicated to them before work commences. |
| Name | Signature | Name | Signature |
| B Small |  | B Small |  |
| M Fitch |  | M Fitch |  |
| T Dawson |  | T Dawson |  |
| Principal Contract Details (The builder or the organisation you are working for.) |
| Principal Contractor (PC): | Project Name: | Date SWMS provided to PC: |
| Project Address: |
| Project Manager (PM): | PM Signature: | CONTACT PH. #: |
| SWMS Scope: This SWMS covers general hazards associated with the operation of a Truck Mounted Hydro-Jet for use in clearing blocked sewers and drains. This includes use of the truck, including prestart and operational use, traffic and pedestrian control, and use of pressurised equipment. This SWMS does not include controls for working in a confined space or pit. A separate, dedicated SWMS must be put in place and utilised for confined space work. |

| This work activity involves the following “High Risk Construction Work” |
| --- |
| ☐ Confined Spaces |  Mobile Plant | ☐ Demolition | ☐ Asbestos |
| ☐ Using explosives | ☐ Diving work | ☐ Artificial extremes of temperature | ☐ Tilt up or pre-cast concrete |
| ☐ Pressurised gas distribution mains or piping chemical, fuel or refrigerant lines energised electrical installations or services |
| ☐ Structures or buildings involving structural alterations or repairs that require temporary support to prevent collapse |
| ☐ Involves a risk of a person falling more than 2m, including work on telecommunications towers |
| ☐ Working at depths greater than 1.5 Metres, including tunnels or mines | ☐ Work in an area that may have a contaminated or flammable atmosphere |
|  Work carried out adjacent to a road, railway or shipping lane, traffic corridor | ☐ In or near water or other liquid that involves risk of drowning |
| Likelihood | Insignificant | Minor | Moderate | Major | Catastrophic | Score | Action | HIERARCHY OF CONTROLS | Most Effective |
| Almost certain | 3 High | 3 High | 4 Acute | 4 Acute | 4 Acute |  |  |  |  |
| Likely | 2 Moderate | 3 High | 3 High | 4 Acute | 4 Acute | 4A Acute | DO NOT PROCEED. |  |  |
| Possible | 1 Low | 2 Moderate | 3 High | 4 Acute | 4 Acute | 3H High | Review before commencing work. |  |  |
| Unlikely | 1 Low | 1 Low | 2 Moderate | 3 High | 4 Acute | 2M Moderate | Maintain control measures. |  |  |
| Rare | 1 Low | 1 Low | 2 Moderate | 3 High | 3 High | 1L Low | Record and monitor. |  | Least Effective |
| Personal Protective Equipment (PPE): Ensure all PPE meets relevant Australian Standards. Inspect, and replace PPE as needed. |
| Foot Protection | Hearing Protection | High Visibility | Head Protection | Eye Protection | Face Protection | Hand Protection | Protective Clothing | Breathing Protection | Sun Protection | fall Arrest | Rings, watches, jewellery that may become entangled in trucks must not be worn. Long and loose hair must be tied back. |
|  |  |  | ☐ |  | ☐ |  | ☐ | ☐ |  | ☐ |  |
| AS 1319-1994 Safety signs for the occupational environment reproduced with permission from SAI Global under licence 1210-c062. Standards may be purchased at http://www.saiglobal.com |

| Job Step | Potential Hazard/s | IR | Control Measures to Reduce Risk | RR | Responsible Person |
| --- | --- | --- | --- | --- | --- |
| Inherent Risk-rating (IR) Residual Risk-rating (RR) |
| Planning & preparation | Lack of consultation may lead to potential outcomes for personal injury, property damage &/or environmental incident. | 3H | Liaise with Principal Contractor to establish the following on-site systems and procedures are in place and take note of: Health and Safety rules Induction for all workers – site specific and toolbox meetings Supervisory arrangements Communication arrangements All relevant workers are appraised for required competencies & for any pre-existing medical conditions if working in remote or isolated locations. PPE required Site plans – showing no go zones for pedestrians Traffic Management Plan Exclusion Zones Risk Assessments SWMS and JSA’s Injury reporting procedures Hazard reporting procedures. | 2M |  |
| Training and Capabilities | Lack of training or the assessment of capability may lead to personal injury, property damage &/or environmental incident. | 3H | Ensure all persons entering a construction site have a General Construction Induction Card (white card) All operators must be licensed and deemed competent on the make/model and type of truck that will be operated Note: In absence of load checking and warning devices, ensure operators are trained to recognise acceptable load distributions Truck must be registered with the State Road and Traffic Authorities prior to use Ensure all relevant workers have undertaken training and/or received instruction in the use of the truck and control measures. Include: All operators are trained in safe and correct methods of operation before including all operational and safety data furnished by the manufacturer. All personnel operating or in the vicinity of the equipment are trained on the hazards and precautions of high-pressure water and compressed air. Reporting procedures for incidents Ensure supervisors, foremen etc. are suitably experienced in the type work to be conducted All workers are trained in this SWMS. Use of supervision where required (e.g. new starters or new equipment) Correct use of equipment including selecting, fitting, use, care of and maintenance. Check workers are in fit condition to work i.e. no signs of fatigue, alcohol or drugs. | 2M |  |
| Pre start check (Pre start Checklist contained in this SWMS) | Lack of a clear assessment may lead to potential personal injury, property damage &/or environmental incident. | 3H | Inspect before use. Ensure: | 2M |  |
|  |  |  | Check that vehicle is in a mechanically sound condition and operator’s instructions are available No evidence of fluid leaks Controls are labelled correctly, legible, functional and able to be locked to “off” position All other items are checked as per manufacturer’s instructions All required safety equipment is fitted and operational All safety guards are in place and undamaged Water tank securely fixed to tray/chassis | Reversing beepers functioning Vehicle break-down equipment: High visibility gear suited for day/night combinations Wet weather gear Traffic cones / signs / reflectors Emergency contact details Mirrors are present, functional and adjusted correctly All stored items in cabin are secured. Pump casing and fittings in good condition. |  |  |
|  |  |  | Do not use if any fault/damage/missing parts. Report immediately and follow tag-out/lock-out procedures. |  |  |
| Truck Operation | Incorrect vehicle use | 3H | Only licensed drivers to drive vehicles Observe road rules at all times Do not exceed weight capacity the vehicle Do not – use mobile phone while driving. Do not – adjust radio channels or volume while driving Drive to the road conditions i.e. slow down when raining or on gravel roads. Avoid road shoulders Watch for vehicles entering from side roads/tracks Give way to approaching trucks/road trains – slow down and move onto shoulder where safe to do so | Monitor/use UHF radio to monitor for changes to site conditions and vehicle movements Wear seat belts at all times when driving Remain attentive - Watch for possible hazards Use mirrors often to monitor the activity around you Drive Smoothly – Be aware of the high centre of gravity of loaded vehicles, Start and stop smoothly. Avoid sharp turns Monitor vehicle constantly for any malfunctions that may affect vehicle performance | 2M |  |
|  | Slips trips and falls | 3H | Face the cabin whenever you mount and dismount the truck Turn off the engine before dismounting. (Even when dismounting to close or open a gate there is a risk of knocking the truck into gear) Ensure the handbrake is always applied or park mode engaged Maintain a three-point contact with the steps and with handholds. Three-point contact can be two feet and one hand Three-point contact can also be one foot and two hands Use provided steps/handholds when entering or exiting cabin (see operations manual) Do not jump off the truck Do not carry tools or supplies when you try to mount / dismount Do not use any controls as handholds when you enter / exit the operator compartment Never mount or dismount a moving truck Never carry another person on the truck unless equipped to do so Never leave operator seat with engine running. | 2M |  |
|  | Pedestrian safety | 4A | Follow Manufacturer’s instructions Site safety rules Traffic control plan Ensure no persons in vicinity before and during start-up and operation Maintain exclusion zone and cease work if approached Travel at appropriate speed for conditions observing speed limits and warning signs Reduce speeds over unexpected hazards. Avoid reversing wherever possible. | 2M |  |
|  | Contact with electricity | 4A | Ensure work is not conducted in close proximity to electrical power lines. Check for: Overhead power lines (including high and low voltage distribution conductors Single wire earth return (SWER) Service cables to premises Communications cables Electrical transformers (mounted lower than cables). Identify maximum range of equipment and how close equipment or load can come to asset (known as design envelope). The following dimensions are taken from the closest point of any extended component of the truck. In general: 3m above, either side and below power lines is No Go Zone Between 3-6.4m of power lines a Spotter is required Further than 6.4m of power lines is open area No work to be conducted within 10m radius of SWER transformer. Spotter required where any part of the truck is within 6.4m of power line. | 2M |  |
|  | Burns / fire damage | 3H | Keep truck free of any excess grease, oil and fuel accumulation Clean up spillage immediately Use only nonflammable solutions for cleaning the truck or components. Store rags and other combustible materials in a safe, fireproof location. | 2M |  |
|  | Hit by moving truck/ Lack of communication | 3H | Ensure an effective system of communication between truck operator and ground workers is established before work commences. Relevant workers must be trained in the procedures involved prior to the work commencing Ground workers are instructed not to approach truck until the operator has agreed to their request to approach. Ensure ground workers are instructed on set distances to maintain from the truck while in operation Ground workers are instructed made familiar with the blind spots of the truck Truck operators and ground workers are required to wear high-visibility clothing. Ensure UHF channel in use on site is known Ensure all personnel are aware of designated work areas and no go zones as defined by the site traffic management plan Communicate with others onsite using designated onsite UHF channel or hand signal. | 2M |  |
| Obtaining Water from Hydrant or other water source e.g. creek/dam | Public safety | 3H | When filling from a hydrant the driver is the controller of the worksite – the area around the hydrant: Park as close to the hydrant as possible Ensure pedestrians have a safe walkway Place temporary barricades/signage in place if pedestrian traffic expected Ensure that the hydrant and standpipe are under observation during the operation If temporary road traffic control is required (e.g. parking on road or pedestrian management): Approvals and permits are sought from local council and/or state road transport departments where necessary Only accredited traffic controllers are to perform traffic control duties All traffic control measures put in place must be implemented as per Australian Standard AS 1742.3–2009: Manual of Uniform Traffic Control Devices, Part 3: Traffic Control for Works on Roads (‘AS 1742.3-2009’) or other requirements as per permit conditions Traffic controllers must have the required accreditation to perform traffic control duties Traffic controllers must have sufficient experience to setup and control traffic safely and efficiently. | 2M |  |
|  | Hit by objects under pressure | 3H | Fitting Standpipe – Obtaining Water from Hydrant - Check standpipe for: Any visible signs of defects Possible leaks – slight “O” ring seal weeps may be acceptable Clear the area around the pit cover plate from debris Remove the pit cover plate and the cover plate on the spring hydrant Lock standpipe in place on hydrant – partial turn Connect flexible hose and ensure couplings are firmly locked in position Open standpipe valve SLOWLY so that all air is expelled from the pipe Reverse the procedure to remove the standpipe. | 2M |  |
|  | Vehicle Roll-over | 3H | When filling and exiting fill area ensure: | Ground is stable, soil is compacted sufficiently Gradient/slope within safe limits for travel. | 2M |  |
|  | Vehicle accident | 3H | Transporting water: Use baffled tanks where possible (prevents water slosh) Never operate a water truck without a thorough understanding of the rules/ traffic management procedures at the construction site Remain attentive - Watch for possible hazards (equipment and workers) Use mirrors often to monitor the activity around you Drive Smoothly – Be aware of the high centre of gravity, and the surge of the water Start and stop smoothly. Make smooth turns and lane changes. Ensure radio is on correct channel and monitored for changes to site conditions and warnings Remember: A half-full tank is more dangerous than a full tank! Ensure travel path (on both road and on site): Allows for height of vehicle Is clear of low-lying tree limbs Is suitable for weight/size of vehicle, limited gradients and slopes Obey speed limits and be aware of increased braking/stopping distance when carrying water | 2M |  |
| Assess onsite conditions for jetting operations | Lack of a clear assessment may lead to personal injury, property damage &/or environmental incident. | 3H | Assess conditions at site on arrival. Ensure: Work site is exactly as detailed in Terms of Agreement or contract Suitable weather conditions Suitable access for all equipment required Suitable ground / track conditions for operation of truck. Flat, even, firm surface, no recently backfilled earth, voids, pits or excavations in close proximity Within manufacturer’s slope/gradient limits Suitable lighting, including night-works (include flood lighting and operator head lamps as applicable) Take note of other vehicle /plant movement Ensure travel path will not damage utilities (gas, telecommunication, electrical, water or sewerage systems) Conduct risk assessment to identify potential hazards such as: | 2M |  |
|  |  |  | Other plant/vehicles Pedestrian traffic Uneven ground, drop-offs | Objects hidden in long grass etc. Steep slopes. |  |  |
|  | Contact with truck or passing vehicles | 3H | Check constantly for changing hazards while working and monitor work position at all times. Ensure: High visibility clothing worn at all times Do not stand behind reversing vehicles Allow sufficient distance from truck during operation (allow sufficient room for equipment failure – such as arm/boom failure or truck rollover) Do not enter established “no go zones” for pedestrians Alertness at all times. Listen for: Reversing alarms/beepers Calls from Truck Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Work positions should be in clear sight of other truck operators Follow traffic management plan requirements. NOTE: Some traffic management plans may say that pedestrians have right-of-way. Never assume this. Make visual and verbal contact with truck operator as required. | 2M |  |
|  | Environmental conditions | 3H | Appropriate protective clothing Wear hand protection Wear non-slip footwear (slippery surfaces) Adequate breaks Check weather conditions – do not work in extreme conditions | Cold: Encourage workers to have adequate warm drinks Access to warm shelter during breaks Heat: Sun brim on hard hat Safety glasses - UV Rated Use 30+ sunscreen on exposed skin areas Adequate drinking water. | 2M |  |
|  | Traffic | 4A | If setting up roadside – comply with local laws and permits Erect any barriers & signage necessary to keep others safe and aware Where temporary road traffic control is required: Approvals and permits are sought from local council and/or state road transport departments where necessary A TMP is developed for the temporary works Only accredited traffic controllers are to perform traffic control duties All traffic control measures must be implemented as per Australian Standard AS 1742.3–2009: Manual of Uniform Traffic Control Devices, Part 3: Traffic Control for Works on Roads (‘AS 1742.3-2009’) or other requirements as per permit conditions Traffic controllers must have the required accreditation to perform traffic control duties Traffic controllers must have sufficient experience to setup and control traffic safely and efficiently. | 2M |  |
| Manhole/pit safety | Trips, slips, falls | 3H | Be aware of ground condition including changes in level, kerb etc. and wet surfaces Wear appropriate non slip covered footwear Never walk backwards when near manholes, pits or other drop offs NEVER wear thongs or similar. | 2M |  |
|  | Lift and removing the pit lid - (MSD) | 3H | High force - heavy pit lid, may be jammed due to accumulation of material or damage: Be aware of sudden unexpected movement if cover dislodging from lid Do not use excessive force Use appropriate tool for cover removal Backhoe and/or crane to assist in lift of heavy lids. | 2M |  |
|  | Hazardous atmospheres | 3H | Allow air to vent from pits when opening covers before commencing work Do not enter any pit A confined space can be defined as an enclosed or partially enclosed space that is likely to be a risk to health and safety, when a person’s head or upper body is within the boundary of the confined space, because of: An atmosphere that does not have a safe oxygen level, or Contaminants, including airborne gases, vapours and dusts, that may cause injury from fire or explosion, or Harmful concentrations of any airborne contaminants. If work involves entering an identified Confined Space, a separate, dedicated ‘Confined Spaces SWMS’ is required to be used in conjunction with this SWMS. Note: Do not enter any manhole/pit in which a person’s head or upper body will be within the space without ensuring a confined space entry permit is issued for each confined space entry requiring: | 2M |  |
|  |  |  | A risk assessment Atmospheric monitoring | Use of respiratory and recovery equipment where indicated if to be entered. |  |  |
|  | Falling into the pit | 3H | If a person has entered or fallen into a manhole DO NOT ENTER THE MANHOLE TO ATTEMPT A RESCUE. Contact the appropriate emergency personnel and the appropriate supervisor immediately if the person cannot be retrieved without entering. | 2M |  |
|  | Crush Injuries | 3H | Never place your hand in the opening to grasp a cover. Get help if necessary and use a tool if available Use blocks/ shims where appropriate to avoid crushing Wear steel-cap boots to protect toes, feet. | 2M |  |
|  | Contact with animals | 3H | Keep your eyes fixed on the ground and be aware of where you are stepping at all times. Never put your hands or feet somewhere where you can’t see them. Check all pits after removing covers Snakes / Spiders - be aware of surroundings, snakes and spiders can be found anywhere Check ground before exiting vehicle: Visually inspect where you are working Check the immediate surroundings before sitting/kneeling or squatting Ensure adequate lighting at all times Make noise Do not approach a snake (dead or alive) | If confronted with a snake or spider: Do not make sudden movements Back away slowly or stay still Allow exit point for snake or spider to escape Do not attack or attempt to harm snake or spider Bee and Wasps - be aware of surroundings (bee’s hives, wasp nests): Note: Wasps nest in logs, walls or underground. They are generally more aggressive than bees and attracted to food and drink Do not contact/disturb nests/hives If nests/hives are located in work area – contact professional to remove before undertaking work. | 2M |  |
| CCTV use | Hit by moving plant /vehicles | 3H | Test unit before use If working roadside or other hazardous area always use a spotter to maintain an awareness of surrounding hazards while focussing on CCTV use. | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Feed camera smoothly, do not jerk or force Avoid any twisting and side-bending during process | Bend knees, not back when carrying and using equipment Avoid awkward and sustained positions. | 2M |  |
| Pumps | Burns | 3H | Always follow pump operating manual Ensure all safety guards and shields are in place while operating pump Do not allow pump to overheat. If pump overheats, turn it off immediately, & allow it to cool Do not touch pump engine or exhaust during or immediately after operation (it will be hot). | 2M |  |
|  | Operator error – Lack of information | 3H | Permanently mount a name plate on pump which provides the following information: | 2M |  |
|  |  |  | Manufacturer’s name Model designation, serial number & year of manufacture Maximum volume and pressure performance | Maximum input speed Maximum operating pressures. |  |  |
|  | Hazardous Atmospheres | 4A | Do not operate motorised machinery in enclosed spaces for extended periods (carbon monoxide build-up) Ensure well-ventilated area when using petrol or diesel pumps. | 2M |  |
| Hydro Jetting | Public access | 3H | A Responsible Person shall be designated for controlling the immediate area where hydro jetting is occurring All operating areas must be barricaded to prevent accidental entry of unauthorised personnel. Use appropriate signage to indicate work being undertaken e.g. - DANGER HIGH PRESSURE WATER BLASTING, KEEP OUT. AUTHORISED PERSONNEL ONLY Entry into the area must be authorised by the Responsible Person The barricade must be far enough from the water blasting to keep observers safe. | 2M |  |
|  | High pressure lacerations/ hit by objects under pressure | 3H | Fluid under pressure can have sufficient force to penetrate skin. If injured by pressurised fluid, obtain medical treatment immediately. The pump unit should not be placed where it can be contaminated by debris from the jetting operation: Use at least two operators when Hydro-jetting. The primary operator handling the cleaning device must maintain control of the water discharge at all times The secondary operator can operate emergency shutdown operations and act as a safety spotter Ensure: All hoses are fitted with actuating devices that require positive effort by the operator, (hand or foot) to keep the supply valve open Hoses used for high pressure cleaning are rated for pressures at least 2.5 times that of the intended operating pressure Hoses must be tagged to indicate: Manufacturers identification Date of manufacture Maximum operating pressure Damaged or faulty hoses shall not be used. It shall be tagged OUT OF SERVICE and repaired or disposed of Using High Pressure Hoses. Ensure: Carefully inspect the nozzle body before each use for damage. Replace damaged or worn nozzles immediately Insert nozzle into the line before pressurising the system. Ensure the nozzle is inserted far enough into the line that any backward facing jets do not pose a hazard to the operator (use an anti-withdrawal device where practicable) During operation, never force a lance through blockages Keep hands and body away from pinholes and nozzles, which eject fluids under high pressure Always depressurise the system before removing the nozzle. Mark the last 3m of the hose in 1.5m sections. (This will allow the operator to determine when the nozzle is close to the entry of the clean out) Take care during insertion and removal a to avoid damage to hoses on corners and sharp edges. (Use edge guards where necessary) Couplings to be securely fastened and reinforced by a secondary method to avoid separation e.g. Whip Check (restrains hose in the event of the end fitting or hose coupling failure). All high-pressure equipment shall be isolated and depressurised before being left unattended. | 2M |  |
|  | Slips, trips and falls | 3H | Ensure plant and equipment placement does not become a trip hazard Access pathways are unobstructed Hoses arranged to minimise tripping hazards. | 2M |  |
|  | Biological hazards - sewers & drains | 4A | Ensure workers are immunised for hepatitis "B" and tetanus Use appropriate PPE - Goggles, face shield, gloves, long sleeves and long pants Use disinfectant to wash hands as per label requirements Immediately treat all abrasions, cuts for contamination. (Seek medical attention for injuries associated with cleaning sewers, drains). Serious illness may occur if this procedure is not followed. | 2M |  |
|  | Hearing loss | 3H | Wear hearing protection, ensure it is: Worn by all persons throughout the period of exposure to noise Suitable for the type of working environment and the work tasks Comfortable and correctly fitting for the worker Regularly inspected and maintained to ensure it remains in good, clean condition. | 2M |  |
| Refueling | Fire / explosion | 3H | Shut off engine Allow to cool before re-fueling if possible Remove cap slowly Use a fuel hose, pouring spout or funnel Fill tank and wipe away excess Ensure there is no over spill Ensure cap has been secured and any vapour residue has been wiped away Check for leaks. DO NOT smoke during re-fuelling Ensure re-fueling is undertaken in well-ventilated area, clear of ignition sources NOTE: Ignition sources include cigarettes, matches/lighters, grinding, welding, power points, lighting, light switches, Material/Safety Data Sheets (M/SDS) for all fuel products on hand Follow manufacturer’s manual/recommendations for re-fuelling Ensure fire extinguisher available and in date. Diesel: Fire extinguisher – Water, foam, dry chemical powder, CO2 Unleaded petrol: Fire extinguisher – Dry chemical powder, foam, CO2. Never use water to extinguish an Unleaded Petrol fire. | 2M |  |
|  | Exposure to hazardous chemicals / substances | 3H | Avoid breathing vapours or contact with fuel If clothing is splashed with fuel, change immediately Do not siphon or swallow fuel as this can be fatal Do not eat, drink or smoke during/after-handling fuel until hands are carefully washed Shower & wash immediately after work. Wash clothes in separate wash from other clothes. | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Where possible use pump to transfer fuel from container into tank. If using fuel container, and lifting into place: | 2M |  |
|  |  |  | Lift smoothly, do not jerk or throw load upwards Avoid any twisting and side-bending during lift | Bend knees, not back. Avoid awkward and sustained positions. |  |  |
|  | Environment incident | 3H | Ensure training in emergency response for chemical spill. Emergency response –fuel spill: Stop the source of the spill or leak or release If that is not possible & it is safe to do so - stop the spill or release from spreading Turn off any ignition sources if safe to do so Use gravel or other material to stop fuel entering drains/water courses Clean up spill as required. | 2M |  |
| On completion | Crush injuries | 3H | Remove keys and inspect equipment for any damage/leaks. If damage is detected – report immediately and take out of service. | 2M |  |
|  | Hit by moving truck | 3H | Store the key in a safe place (restrict unauthorised access) Ensure truck is parked in a safe, level area, clear of unstable or sloping ground. | 2M |  |
|  | Environmental contaminants | 3H | Ensure all equipment /truck is washed free of dirt, vegetation, debris before leaving site Ensure any contaminated wastewater is captured as per Local and State Environment Laws Do not wash truck where residue can enter and sensitive areas such as storm water drains and water-ways Avoid cross contamination: Disassemble and clean all equipment Dispose of all waste in accordance with regulations Maintain an M/SDS for all chemicals used. | 2M |  |
|  | Public safety | 3H | Report any damage or malfunction of the unit or components. If acceptable, remove any barricades or signs, contact supervisor and return as agreed. | 2M |  |
| Truck Roll-over – emergency response |
| Establish communication with victims (if applicable) and maintain for entire rescue. Conduct response as required for specific conditions at site. Operator: Do not attempt to jump from vehicle during roll-over – remain in seat with seatbelt on After incident has occurred, if able, turn off engine Remain in position with seatbelt on until help arrives, unless it is safe to exit cabin If it is safe and injuries permit, exit cabin without jumping, and move clear from plant. | Personnel: Clear non-essential persons from area Check for fuel and/or fluid leaks. Ensure there are no ignition sources Check for fire or fire/explosion risks. Use suitable fire protection equipment to control fire (if safe to do so) Do not approach the vehicle until Emergency Responders attend the scene. Note: Vehicle may be unstable and unsafe to approach. Do not place first responders at risk – await assistance from suitably trained and resourced Emergency Responders. |

| Truck Pre-start Checklist |
| --- |
| Name of Plant: | Identification or Registration No. | Date: |
| ITEM | Yes | No | N/A | ITEM | Yes | No | N/A |
| Daily logbook completed | ☐ | ☐ | ☐ | Instruction manual available | ☐ | ☐ | ☐ |
| Operator licensed to operate | ☐ | ☐ | ☐ | Cabin | Safe access/exit | ☐ | ☐ | ☐ |
| Fluid Levels | Hydraulics | ☐ | ☐ | ☐ |  | Clean, free of clutter | ☐ | ☐ | ☐ |
|  | Oils | ☐ | ☐ | ☐ |  | Ventilated / AC | ☐ | ☐ | ☐ |
|  | Water | ☐ | ☐ | ☐ |  | Visibility from cabin windows | ☐ | ☐ | ☐ |
|  | Fuel | ☐ | ☐ | ☐ |  | Loose objects secured/removed | ☐ | ☐ | ☐ |
| Fluid leaks | Hydraulics | ☐ | ☐ | ☐ | Water Tank/pumps | Good condition no leaks | ☐ | ☐ | ☐ |
|  | Oils | ☐ | ☐ | ☐ |  | Fittings/valves good condition | ☐ | ☐ | ☐ |
|  | Water | ☐ | ☐ | ☐ |  | Hoses/couplings | ☐ | ☐ | ☐ |
|  | Fuel | ☐ | ☐ | ☐ |  | Pump fueled / check starts and runs | ☐ | ☐ | ☐ |
| Danger areas guarded | Moving motor parts | ☐ | ☐ | ☐ | Tank securely fixed to tray ( tipper models) | ☐ | ☐ | ☐ |
|  | Shafts | ☐ | ☐ | ☐ | Traffic/Pedestrian control equipment | ☐ | ☐ | ☐ |
|  | Hydraulic hoses/valves etc. | ☐ | ☐ | ☐ | Locking pins in place | ☐ | ☐ | ☐ |
|  | Hot engine/muffler parts | ☐ | ☐ | ☐ | Gauges / Lamps / Warning systems | ☐ | ☐ | ☐ |
| Tyres / wheels / tracks | Correct type | ☐ | ☐ | ☐ | Lights – front / rear/ stop / turning / beacons | ☐ | ☐ | ☐ |
|  | Do not have cracks | ☐ | ☐ | ☐ | Horns / reversing alarms | ☐ | ☐ | ☐ |
|  | Have adequate tread depth | ☐ | ☐ | ☐ | Brakes – park / foot / emergency | ☐ | ☐ | ☐ |
|  | Correct and equal pressure | ☐ | ☐ | ☐ | Fire extinguisher | ☐ | ☐ | ☐ |
| Warning devices | Installed | ☐ | ☐ | ☐ | Spill kit | ☐ | ☐ | ☐ |
|  | Positioned for best affect | ☐ | ☐ | ☐ | Report any problems to supervisor and follow tag-out/lock-out procedures for unsafe equipment. Comments: |
| Other? | ☐ | ☐ | ☐ |  |
| Repairs completed | ☐ | ☐ | ☐ |  |
| Operators Name: |  |
| Operators Signature: |  |

| Emergency Response - Call 000 immediately. |
| --- |
| If work is to be conducted on a construction site (or a site controlled by another Employer / PCBU) follow the site-specific Emergency Management Plan. Ensure: Adequate numbers of first aid trained staff are on site when working at heights occurs First aiders are trained and competent in managing injuries associated with demolition until emergency services arrive All rescue equipment is in good condition, available for use and in close proximity to the work site. | Ensure workers have access to: First aid kit/supplies First Aid trained personnel familiar with Resuscitation and emergency response for electric shock M/SDS Communication devices (check mobile phones will have service in area) Suitable fire protection equipment. |
| Safe Work Method Statement (SWMS) Part 2 |
| Formal Training, Licences required for workers undertaking this task: | Relevant Legislation & Codes of Practice Retain only the legislation references applicable to your state of operation for this SWMS. |
| Delete or add as relevant Licence to Perform High Risk Work (operating certain truck, equipment) TAFE or other recognised training organisation Construction Induction Card (or equivalent) Competent in operation of make/model of truck Emergency procedures – emergency response PPE Traffic Management Plans | Commonwealth, NSW, QLD, ACT Work Health and Safety Act 2011 Work Health and Safety Regulations 2011 Northern Territory Work Health and Safety (National Uniform Legislation) Act 2011 Work Health and Safety (National Uniform Legislation) Regulations SA, Tasmania Work Health and Safety Act 2012 Work Health and Safety Regulations 2012 Codes of Practice: Safe Work Australia (2011): Construction Work First Aid in the Workplace Managing the Risk of Falls at Workplaces Managing the Risk of Truck in the Workplace Managing Noise and Preventing Hearing Loss in the Workplace How to Manage Work Health and Safety Risks Hazardous Manual Tasks Managing Risks of Hazardous Chemicals Managing Electrical Risks in the Workplace Managing the Work Environment and Facilities WHS Consultation, Cooperation & Coordination | Victoria: Occupational Health & Safety Act 2004 Occupational Health & Safety Regulations 2007 Compliance Codes: WorkSafe Victoria (2008): Compliance Code: Communicating OHS Across Languages First Aid in the Workplace Prevention of Falls in General Construction Workplace Amenities and Work Environment Codes of Practice: WorkSafe Victoria (1990): No. 13: Building and Construction Workplaces (2000): No. 25: Manual Handling (1995): No. 19: Truck (1998): No. 23: Truck (Amendment No. 1) (2004): No. 29: Prevention of Falls in Housing Construction (2000): No. 24: Hazardous Substances Western Australia Occupational Safety & Health Act 1984 Occupational Safety & Health Regulations 1996 Codes of Practice: |
| Details of Supervisory Arrangements for workers undertaking this task: |  |  |
| Delete or add as relevant Suitably qualified supervisors for job Direct on-site supervision Remote site – communication systems/ schedule Audits Spot Checks, etc. Reporting systems |  |  |
| Details of: regulatory permits/licenses Engineering Details/Certificates/WorkCover. Approvals: |  |  |
| Delete or add as relevant Local council permits Authorisation to work Confined Space Permit Building Approvals EPA approvals/permits Certain truck to be registered with State Authority PPE to comply with relevant Australian Standards |  |  |
|  | Truck/Tools/Equipment List for the job. | Reference Documents |
|  | (Make & Model) |  |

| Safe Work Method Statement (SWMS) Part 3 |
| --- |
| This SWMS has been developed in consultation and cooperation with employee/workers and relevant Employer/Persons Conducting Business or Undertaking (PCBU). I have read the above SWMS and I understand its contents. I confirm that I have the skills and training, including relevant certification to conduct the task as described. I agree to comply with safety requirements within this SWMS including risk control measures, safe work instructions and Personal Protective Equipment described. |
| Overall Risk Rating after Controls | 1 Low | 2 Moderate | 3 High | 4 Acute |
| Employee/Worker Name | Job Role / Position | Signature | Date | Time | Employer/PCBU/ Supervisor |

| Review: Ensure all controls are reviewed as per the following: If controls fail to reduce risk adequately When changes to the workplace or work activity occur that create new / different risks where controls may no longer be effective New hazards identified After an incident involving work activities relevant to this SWMS During consultation with relevant persons indicate review is needed A Health and Safety Representative (HSR) requests a review in line with the requirements of the legislation. | Monitor: To ensure controls are implemented and monitored effectively: Toolbox /pre-work meetings will be undertaken Relevant persons will be consulted on hazards and contents of SWMS, work plans and other applicable information Control measures will be monitored throughout works: *Spot checks *Consultation *Scheduled audits Corrective actions will be recorded and rectified in a timely manner SWMS will be reviewed and updated accordingly (in consultation with relevant persons). |
| --- | --- |
| Review No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Name: |  |  |  |  |  |  |  |  |  |  |
| Initial: |  |  |  |  |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |  |  |  |  |