| Safe Work Method Statement (SWMS) Part 1 |
| --- |
| Activity: Handheld power tools operation on construction sites | SWMS #: |
| Business Name: Bowley Plumbing Services | ABN: 97 007 937 439 |
| Business Address: 19 Swallow Ave, Modbury Heights SA |
| Business Contact: Phillip Bowley | Phone #: 0418 891 498 |
| SWMS Approved by: Employer / PCBU / Director / OWNER. |
| Name: Phillip Bowley |
| Signature: | Date: |
| Person/s responsible for ensuring compliance with SWMS: Phillip Bowley and all employees |
| Person/s responsible For reviewing the SWMS: Phillip Bowley |
| Relevant workers consulted in the development, approval and communication of this SWMS. | All Persons involved in the task must have this SWMS communicated to them before work commences. |
| Name | Signature | Date | Tool Box Talks will be undertaken to identify, control and communicate additional site hazards. |
| B Small |  |  | Work must cease immediately if incident or near miss occurs. SWMS must be amended in consultation with relevant persons. |
| M Fitch |  |  | Amendments must be approved by Phillip Bowley and communicated to all affected workers before work resumes. |
| T Dawson |  |  | SWMS must be made available for inspection or review as required by WHS legislation. |
|  |  |  | Record of SWMS must be kept as required by WHS legislation (until job is complete or for 2 years if involved in a notifiable incident). |
| Principal Contractor Details (The builder or the organisation you are working for.) |
| Principal Contractor (PC): | Project Name: | Date SWMS provided to PC: |
| Project Address: |
| Project Manager (PM): | PM Signature: | CONTACT PH. #: |
| SWMS Scope: This SWMS covers general safety issues concerned with the operation of hand held power tools. Examples of power tools include: Drills (electric, pneumatic, battery operated etc.), Chainsaws, Portable power tools, Angle grinders, Etc. |

| This work activity involves the following “High Risk Construction Work” |
| --- |
| ☐ Confined Spaces |  Mobile Plant | ☐ Demolition | ☐ Asbestos |
| ☐ Using explosives | ☐ Diving work | ☐ Artificial extremes of temperature | ☐ Tilt up or pre-cast concrete |
| ☐ Pressurised gas distribution mains or piping chemical, fuel or refrigerant lines energised electrical installations or services |
| ☐ Structures or buildings involving structural alterations or repairs that require temporary support to prevent collapse |
| ☐ Involves a risk of a person falling more than 2m, including work on telecommunications towers |
| ☐ Working at depths greater than 1.5 Metres, including tunnels or mines | ☐ Work in an area that may have a contaminated or flammable atmosphere |
| ☐ Work carried out adjacent to a road, railway or shipping lane, traffic corridor | ☐ In or near water or other liquid that involves risk of drowning |
| Likelihood | Insignificant | Minor | Moderate | Major | Catastrophic | Score | Action | HIERARCHY OF CONTROLS | Most Effective |
| Almost certain | 3 High | 3 High | 4 Acute | 4 Acute | 4 Acute |  |  |  |  |
| Likely | 2 Moderate | 3 High | 3 High | 4 Acute | 4 Acute | 4A Acute | DO NOT PROCEED. |  |  |
| Possible | 1 Low | 2 Moderate | 3 High | 4 Acute | 4 Acute | 3H High | Review before commencing work. |  |  |
| Unlikely | 1 Low | 1 Low | 2 Moderate | 3 High | 4 Acute | 2M Moderate | Maintain control measures. |  |  |
| Rare | 1 Low | 1 Low | 2 Moderate | 3 High | 3 High | 1L Low | Record and monitor. |  | Least Effective |
| Personal Protective Equipment (PPE): Ensure all PPE meets relevant Australian Standards. Inspect, and replace PPE as needed. |
| Foot Protection | Hearing Protection | High Visibility | Head Protection | Eye Protection | Face Protection | Hand Protection | Protective Clothing | Breathing Protection | Sun Protection | fall Arrest | Rings, watches, jewellery that may become entangled in machines must not be worn. Long and loose hair must be tied back. |
|  |  |  |  |  |  |  |  |  |  | ☐ |  |
| AS 1319-1994 Safety signs for the occupational environment reproduced with permission from SAI Global under licence 1210-c062. Standards may be purchased at http://www.saiglobal.com |

| Job Step | Potential Hazard/s | IR | Control Measures to Reduce Risk | RR | Responsible Person |
| --- | --- | --- | --- | --- | --- |
| Inherent Risk-rating (IR) Residual Risk-rating (RR) |
| Planning & preparation | Lack of consultation with potential outcomes for personal injury, property damage &/or environmental incident. | 3H | Liaise with Principal Contractor to establish the following on-site systems and procedures are in place and take note of: Health and Safety rules Induction for all workers – site specific and toolbox meetings Supervisory arrangements Communication arrangements All relevant workers are appraised for required competencies & for any pre-existing medical conditions if working in remote or isolated locations. PPE required Site plans – showing no go zones for pedestrians Traffic Management Plan Exclusion Zones Risk Assessments SWMS and JSA’s Injury reporting procedures Hazard reporting procedures. | 2M |  |
| Training and Capabilities | Lack of training or the assessment of capability may lead to personal injury, property damage &/or environmental incident. | 3H | Ensure all persons entering site have a General Construction Induction Card (white card). Ensure all relevant workers have undertaken training and/or received instruction in the use of control measures. Include: Reporting procedures for incidents Correct use of equipment including selecting, fitting, use, care of and maintenance Correct use of all tools used Use of supervision where required (e.g. new starters or new equipment) Ensure supervisors, foremen etc. are suitably experienced in the type work to be conducted All workers are trained in this SWMS. All relevant workers involved in the use of handheld power tools must be suitably trained and deemed competent to operate the tool. Training of operators must include: Review of operating manual Comprehensive operating instructions Location of guards Adjustment of guards Removal of guards for maintenance work including restrictions on who may do the work Actions, including who and how to notify, if a guard is found removed or missing Practical instructions on how to replace blade. If working on EWPs or scaffolding, for this task, ensure there are separate, dedicated EWP/Scaffolding SWMS and that all workers/employees have relevant training and licensing. | 2M |  |
| Assess onsite conditions | Lack of a clear assessment may lead to personal injury, property damage &/or environmental incident. | 3H | Assess conditions at site on arrival. Ensure: Ensure site-specific induction is undertaken (include location of amenities, first aid facilities, emergency plans and evacuation points, incident reporting, communication, contact persons etc.) Assess mobile phone reception (alternative emergency communications procedures in place if no reception available) Work site is exactly as detailed in Terms of Agreement or contract Suitable weather conditions (do not work outside in low visibility, heavy rain, high winds etc.) Suitable access for all equipment required Suitable space for operation of equipment Suitable lighting, including night-works (include flood lighting and operator head lamps as applicable) Take note of mobile plant movement. Conduct site inspection to identify potential hazards such as: Work at heights (above 2m) Lighting Ventilation Dust Temperature etc. Exposed electrical switchboards/power points Duration of manual handling tasks (such as working with arms above shoulder height). | 2M |  |
| Tool selection | Increased hazards relating to the use of unsuitable tool for the task | 3H | Suited to the material. E.g.: steel, wood, MDF, plastic Not too powerful for task. E.g.: don’t use larger angle grinder than needed Sufficient power for task – excessive force not required. Low impact tools where possible Select tools with lower decibel readings. | 2M |  |
| Using grinders, metal cutting tools etc. | Fire | 4A | Attain Hot Work Permit from responsible person: Ensure completed Hot Work Permit available at site Follow safety precautions on Hot Work Permit Note: Do not conduct work that is not listed on Hot Work Permit. If other Hot Works are required, obtain Hot Work Permit for that task before commencement. | 2M |  |
| Work area set up | Other workers / public safety | 3H | Keep bystanders away while operating the power tool, set up exclusion zones. | 2M |  |
|  | Environmental incident / property damage from fire | 3H | When using tools that create sparks or embers. Ensure not within 15m of: Grass/vegetation/timber and other combustibles Flammables storages Gas maintenance access points Storm water drains Rivers or sensitive environmental areas Pressure vessels and tanks (including pipelines, flanges, vents and valves) Check weather requirements Do not conduct Hot Works in high temperatures, high winds or on days of Total Fire Bans. | 2M |  |
|  | Contact with mobile plant or passing vehicle | 3H | Check constantly for changing hazards while working and monitor work position at all times. Ensure: High visibility clothing worn at all times Do not stand behind reversing vehicles Allow sufficient distance from plant during operation (allow sufficient room for equipment failure – such as arm/boom failure or plant rollover) No work is conducted in established “no go zones” for pedestrians Alertness at all times. Listen for: Reversing alarms/beepers Calls from Plant Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Work positions should be in clear sight of plant operators Follow traffic management plan requirements. NOTE: Some traffic management plans may say that pedestrians have right-of-way. Never assume this. Make visual and verbal contact with plant operator as required. | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Work station is set-up ergonomically where possible (avoid reaching too high, low, over-reaching or other awkward postures) Provide trestles / benches to place work pieces on to reduce manual handling risks (between shoulder and knee height) Ensure materials / equipment is as close to work area as possible. | 2M |  |
|  | Slips, trips & falls on the same level | 3H | Ensure: Sufficient lighting All trip hazards / obstructions removed from work area The work area is not wet under foot Keep electrical cords clear of excessive heat, oil, sharp edges (including moving parts of tools) Use pendants, lead stand or insulated cable hangers Do not drape leads over body or work piece or any metal surface Do not run leads along ground/floor, near sharp edges, across doorways or hang them over metal structures. | 2M |  |
|  | Dust | 3H | Always operate tool in well-ventilated area. | 2M |  |
|  | Struck by falling objects | 3H | Ensure sturdy work surface (use vice, clamps as required). | 2M |  |
|  | Work adjacent to road & public safety | 4A | Park working vehicle in driveway or allocated parking to avoid travelling across roads when delivery working equipment If setting up roadside – comply with local laws and permits Erect any barriers & signage necessary to keep others safe and aware. | 2M |  |
|  | Property damage Fire / explosion | 3H | Ensure equipment rated for atmospheric requirements (water, or explosion-proof for flammable zones) Ensure fire protection equipment accessible as required Ensure equipment is not placed in areas where they may be run over, damaged or exposed to water (unless rated for wet environments). Keep power leads up off the ground and out of the way Do not use drums or containers that stored flammables to secure work piece onto. | 2M |  |
|  | Contact with electricity | 3H | All power tools and leads are Tested and Tagged and are current Safety switches (RCD’s) are provided Ensure switchboards have appropriately rated circuit breaker Pre-inspect equipment If equipment is damaged, do not use Take out of service, apply Lock-out/tag-out (LOTO) procedures and inform supervisor immediately. Do not use plug top RCD’s fitted to power tools as the RCD cannot be tested. | 2M |  |
|  | Contact with hazardous chemicals / substances | 3H | Ensure current Material/Safety Data Sheets (M/SDS) are obtained for all hazardous chemicals/substances and accessible on site. E.g. MDF (Medium Density Fibreboard), Lubricants for maintenance etc. | 2M |  |
| Operating the power tool | Cuts, laceration, amputation | 4A | E.g. Power saw. Always ensure that the tool is switched off and power isolated before pre-start check, adjusting, changing set-ups or repairing. Allow the blade to reach full speed before cutting, do not force the blade and always start the cut gently. | 2M |  |
|  |  |  | Ensure: Blade has fully stopped turning before placing the tool down The lower guard has retracted to the closed position. | NEVER: Operate the tool with the retractable guard tied back or the trigger tied on Place hands under the work piece being cut Ensure the switch is in the “off” position before plugging it in to avoid accidental starting. |  |  |
|  |  |  | Stay alert – concentrate on what you are doing at all times and be aware of kickback You must keep your off hand out of the path of the tool in any case. NOTE: Always turn off the tool when not in use. |  |  |
|  | Contact with electricity | 4A | Ensure: Do not: | Isolate from power before cleaning or making adjustments Keep electric cord away from heat, oil, sharp edges or moving parts Replace damaged cords immediately Never carry electrical tools by power cord Do not use power cord to pull equipment from power socket Unplug tool when not in use Check for damage or faults regularly during operation. Examples, if excessive vibration occurs, stop using immediately. Expose power tool to rain or wet conditions Abuse the cord, never use the cord to carry the tool or pull the plug from the outlet. | 2M |  |
|  | Fire / explosion | 3H | Do not operate power tools in explosive atmospheres (i.e. presence of flammable liquids, gases or dust) Check that sparks do not enter flammable storage areas. | 2M |  |
|  | Dust | 3H | Wear eye and breathing protection Local exhaust extraction is provided (if required) Vacuum attachment/bag fitted (if required). | 2M |  |
|  | Kickback causing a piece of material into a projectile | 3H | Stay alert – concentrate on what you are doing at all times and be aware of kickback Kickback occurs more often with small workpieces Check to make sure the tool is functioning properly. | 2M |  |
|  | Slips, trips & falls on the same level | 3H | Do not leave tools on floor Remove off cuts clear of work area and maintain housekeeping Power cord does not pose a tripping hazard to operator (pendulum plugs preferred). | 2M |  |
|  | Noise | 3H | Obtain silencers or other components to reduce noise (such as insulation). Wear hearing protection as required, ensure it is: Worn by all persons throughout the period of exposure to noise Suitable for the type of working environment and the work tasks Comfortable and correctly fitting for the worker Regularly inspected and maintained to ensure it remains in good, clean condition. | 2M |  |
|  | Contact with hot surfaces | 3H | Do not touch the tool immediately after operation, it may be extremely hot causing burns Wear hand protection. | 2M |  |
|  | Vibration / Muscular stress / MSD | 3H | Provide tools with anti-vibration or anti-kickback features where possible Select suitable size, weight, type of handle, grip etc. Use vibration-absorbing gloves as required (particularly in cold weather) Suspend / support heavier tools if used repetitively Ensure triggers are long enough (approx. 5cm long) to allow activation by several fingers Use triggers that can lock into place for use over longer periods (more than 30 seconds at a time) Ensure handles: Are cylindrical and approx. 4cm in diameter Allow wrist to remain straight Comfortable grip No sharp edges Grip length approx. 12cm Avoid repetitive tasks. Ensure: Job rotation Sufficient breaks Do not work in awkward or static postures for more than 30 minutes at a time or 2 hours over entire shift. | 2M |  |
| Working with hazardous materials | Asbestos | 4A | Wear required PPE and respiratory protective equipment (RPE): Inspection – P1 or P2 half face (can be either disposable or cartridge) Sample removal / drilling – P1 or P2 half face (can be either disposable or cartridge). Use a non-powered hand drill or low speed battery-powered drill where possible (do not use high speed drill). Battery powered drills should be fitted with a local exhaust ventilation (LEV) dust control hood wherever possible. The following items are prohibited: High speed power or pneumatic tools such as grinders or power saws High pressure water cleaners Brooms and brushes (unless these items are used for sealing purposes) Compressed air. | 2M |  |
|  | Lead | 4A | Current M/SDS, determine if any materials / items used or handled or any processes undertaken at the workplace involve Lead, including the generation of Lead fumes or dust and / or the accumulation of materials or items containing Lead. Wear relevant PPE recommended in the M/SDS In addition to standard work area setup ensure to have: Water / sinks available Restricted area - no access by general public or unauthorised workers Warning signage if required No ignition sources No incompatible chemicals in close proximity Area kept clean That contamination by Lead is confined Clean up spills immediately and dispose of contaminated material properly. | 2M |  |
|  | Crystalline silica (found in concrete, granite and stone) | 4A | Use wet cutting methods Wear respirator protection as required Wear disposable or washable protective clothing: Vacuum the dust from the clothes or change before into clean clothes before leaving the worksite Wash hands before eating, drinking, smoking or applying cosmetics in areas where crystalline silica is present. | 2M |  |
| Working at elevated levels | Struck by falling objects | 3H | Use caution when working at elevated levels: Avoid using tools when working from a ladder. Consider use of elevated work platform (EWP). Use tool lanyards to pass tools to persons at height and ensure tools cannot fall onto workers below. Ensure kickboards installed on elevated work areas to prevent tools falling off. | 2M |  |
|  | Slips, trips, falls causing injury | 3H | Identify all hazards. Consider: | Ground/floor surface condition Experience of workers Weather conditions (rain, wind loads, fog, dew) Where ground surfaces may change level Check design to ensure that the equipment will support a specified load – or ‘duty rating’. This must be clearly stated on the item Use all height-access equipment as per manufacturer’s instructions and for its designed purpose. | 2M |  |
|  | Fall from ladder | 3H | Work positioning. Ensure: Load rating of at least 120kg Correct size and length for job No damage, clean and dry Secured to work site (base and top) Metallic, wire- reinforced or conductive ladders should be avoided around live electrical equipment Face ladder when ascending/descending Ensure 3 points of contact remain on ladder at all times Ensure only 1 person working from each ladder. | 2M |  |
|  | Fall from platform ladder | 3H | Ensure: Trestle back undamaged If unfolding type, chains, rivets etc are undamaged and functional Suitable height hand rail (900mm) Triangular flat plate bracing Correct size for job (platform level) Non-slip treads Large feet with non-slip mouldings Non-slip platform of sufficient strength for persons, tools and equipment Industrial rating. | 2M |  |
|  | Fall from trestle | 3H | Trestles must: Be rated for proposed weight and span Have an overhang of at least 150 mm and not more than 250mm at each end and be “locked” together. Example - clamped near the centre span to prevent individual movement. Have an unobstructed surface width of at least 450mm (two planks wide) Must be matched pairs i.e. the rungs should be equivalent heights and spacing. | 2M |  |
| Remote and/or isolated work | Personal Injury from delay in emergency assistance to remote workers | 3H | A ‘Buddy’ system is utilised for high-risk tasks undertaken in remote locations or working in isolation. A procedure is developed and in place for regular contact with people working remotely or in isolation, The procedure should identify: Travel itineraries, locations, scheduled contact persons and times Sufficient supplies of water, food, fuel & supplies needed An emergency response Appropriate Vehicles Safety equipment including first aid. | 2M |  |
|  |  |  | Add any site-specific hazards, which have not been identified in this SWMS. |  |  |
| On completion | Slips, trips, falls causing injury | 3H | Clean up tools and secure into working toolbox/vehicle Clean work area of off-cuts Sweep up all dust (avoid the use of compressed air) and /or empty extraction bags. | 2M |  |
|  | Contact with electricity | 3H | Disconnect power tool/extension leads from power point before winding up, so that you don’t get a shock if the lead is damaged Inspect leads and power equipment for damage If safe to do so, remove isolation locks/tags and test appliance for function. | 2M |  |
|  | Contamination of waterways | 3H | Dispose of waste timber and dust to skips/bins provided. | 2M |  |
|  | Public safety | 3H | If acceptable, remove barricades, contact supervisor and return as agreed. | 2M |  |

| Emergency Response - Call 000 immediately. |
| --- |
| If work is to be conducted on a construction site (or a site controlled by another Employer / PCBU) follow the site-specific Emergency Management Plan. Ensure: Adequate numbers of first aid trained staff are on site when working at heights occurs First aiders are trained and competent in managing injuries associated with demolition until emergency services arrive All rescue equipment is in good condition, available for use and in close proximity to the work site. | Ensure workers have access to: First aid kit/supplies First Aid trained personnel familiar with Resuscitation and emergency response for electric shock M/SDS Communication devices (check mobile phones will have service in area) Suitable fire protection equipment. |
| Safe Work Method Statement (SWMS) Part 2 |
| Formal Training, Licences required for workers undertaking this task: | Relevant Legislation & Codes of Practice Retain only the legislation references applicable to your state of operation for this SWMS. |
| Delete or add as relevant Licence to Perform High Risk Work (operating certain plant, equipment) TAFE or other recognised training organisation Construction Induction Card (or equivalent) Competent in operation of make/model of plant Emergency procedures – emergency response PPE Traffic Management Plans | Commonwealth, NSW, QLD, ACT Work Health and Safety Act 2011 Work Health and Safety Regulations 2011 Northern Territory Work Health and Safety (National Uniform Legislation) Act 2011 Work Health and Safety (National Uniform Legislation) Regulations SA, Tasmania Work Health and Safety Act 2012 Work Health and Safety Regulations 2012 Codes of Practice: Safe Work Australia (2011): Construction Work First Aid in the Workplace Managing the Risk of Falls at Workplaces Managing the Risk of Plant in the Workplace Managing Noise and Preventing Hearing Loss in the Workplace How to Manage Work Health and Safety Risks Hazardous Manual Tasks Managing Risks of Hazardous Chemicals Managing Electrical Risks in the Workplace Managing the Work Environment and Facilities WHS Consultation, Cooperation & Coordination | Victoria: Occupational Health & Safety Act 2004 Occupational Health & Safety Regulations 2007 Compliance Codes: WorkSafe Victoria (2008): Compliance Code: Communicating OHS Across Languages First Aid in the Workplace Prevention of Falls in General Construction Workplace Amenities and Work Environment Codes of Practice: WorkSafe Victoria (1990): No. 13: Building and Construction Workplaces (2000): No. 25: Manual Handling (1995): No. 19: Plant (1998): No. 23: Plant (Amendment No. 1) (2004): No. 29: Prevention of Falls in Housing Construction (2000): No. 24: Hazardous Substances Western Australia Occupational Safety & Health Act 1984 Occupational Safety & Health Regulations 1996 Codes of Practice: |
| Details of Supervisory Arrangements for workers undertaking this task: |  |  |
| Delete or add as relevant Suitably qualified supervisors for job Direct on-site supervision Remote site – communication systems/ schedule Audits Spot Checks, etc. Reporting systems |  |  |
| Details of: regulatory permits/licenses Engineering Details/Certificates/WorkCover. Approvals: |  |  |
| Delete or add as relevant Local council permits Authorisation to work Confined Space Permit Building Approvals EPA approvals/permits Certain plant to be registered with State Authority PPE to comply with relevant Australian Standards |  |  |
|  | Plant/Tools/Equipment List for the job. | Reference Documents |
|  | (Make & Model) |  |

| Safe Work Method Statement (SWMS) Part 3 |
| --- |
| This SWMS has been developed in consultation and cooperation with employee/workers and relevant Employer/Persons Conducting Business or Undertaking (PCBU). I have read the above SWMS and I understand its contents. I confirm that I have the skills and training, including relevant certification to conduct the task as described. I agree to comply with safety requirements within this SWMS including risk control measures, safe work instructions and Personal Protective Equipment described. |
| Overall Risk Rating after Controls | 1 Low | 2 Moderate | 3 High | 4 Acute |
| Employee/Worker Name | Job Role / Position | Signature | Date | Time | Employer/PCBU/ Supervisor |

| Review: Ensure all controls are reviewed as per the following: If controls fail to reduce risk adequately When changes to the workplace or work activity occur that create new / different risks where controls may no longer be effective New hazards identified After an incident involving work activities relevant to this SWMS During consultation with relevant persons indicate review is needed A Health and Safety Representative (HSR) requests a review in line with the requirements of the legislation. | Monitor: To ensure controls are implemented and monitored effectively: Toolbox /pre-work meetings will be undertaken Relevant persons will be consulted on hazards and contents of SWMS, work plans and other applicable information Control measures will be monitored throughout works: *Spot checks *Consultation *Scheduled audits Corrective actions will be recorded and rectified in a timely manner SWMS will be reviewed and updated accordingly (in consultation with relevant persons). |
| --- | --- |
| Review No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Name: |  |  |  |  |  |  |  |  |  |  |
| Initial: |  |  |  |  |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |  |  |  |  |

# Text boxes

Do not:

- Attempt to move or extend ladder when on it

- Slide down stiles

- Step up or down two or more rungs at a time